## Slide 1: WF on assistant information for RRM measurement enhancement
LG Electronics, …
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd -7th April 2017
Agenda item 7.2.7.2
R1-1706618

## Slide 2: Background
In RAN#75, a new WID on further NB-IoT enhancements was approved. According to the WID, following was agreed on narrowband measurement accuracy improvements:
  “Evaluate and if appropriate specify use of additional existing signals than NRS for RRM measurements, with associated RAN4 core requirements taking into account e.g. UE complexity, power consumption, system capacity”
In this meeting(RAN1 #88bis) on Tuesday, RAN1 agreed
  At least NSSS is used additionally to NRS for in-band, guard-band, standalone.
    FFS details of related signaling

## Slide 3: Proposal
For the enhanced RRM measurement with NSSS, the following information should be conveyed to the UE (individually or jointly) for the serving cell and neighbor cells.
  applicability of enhanced RRM measurement with NSSS
  transmission power offset of NSSS over NRS
  FFS applicability of coherent combining of NSSS and NRS
FFS if the following information is provided for further enhanced RRM measurement
  valid DL subframes of neighbor cells
  number of NRS antenna ports of neighbor cells
  applicability of NRS in another carrier in addition to the serving carrier