## Slide 1: WF on beam reporting
CATT, Intel
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd - 7th April 2017
Agenda: 8.1.2.2.1
R1-1706660

## Slide 2: Background
Working assumptions:
Support at least one of these two alternatives of beam reporting:
  Alt 1:
  UE reports information about TRP Tx Beam(s) that can be received using selected UE Rx beam set(s).
    where a Rx beam set refers to a set of UE Rx beams that are used for receiving a DL signal
      Note: It is UE implementation issues on how to construct the Rx beam set.
      One example: each of Rx beam in a UE Rx beam set corresponds to a selected Rx beam in each panel.
    For UEs with more than one UE Rx beam sets, the UE can report TRP Tx Beam(s) and an identifier of the associated UE Rx beam set per reported TX beam
    NOTE: Different TRP Tx beams reported for the same Rx beam set can be received simultaneously at the UE.
    NOTE: Different TRP TX beams reported for different UE Rx beam set may not be possible to be received simultaneously at the UE
  Alt 2:
  UE reports information about TRP Tx Beam(s) per UE antenna group basis
    where UE antenna group refers to receive UE antenna panel or subarray
    For UEs with more than one UE antenna group, the UE can report TRP Tx Beam(s) and an identifier of the associated UE antenna group per reported TX beam
    NOTE: Different TX beams reported for different antenna groups can be received simultaneously at the UE.
    NOTE: Different TX beams reported for the same UE antenna group may not be possible to be received simultaneously at the UE
FFS: How UE antenna group or Rx beam set is captured in the specification

## Slide 3: Background
Agreements:
Confirm the working assumption on group based beam reporting made in RAN1 Jan. NR Adhoc Meeting, with the following update:
  Further discussion for possible down-selection or merging, especially taking into account overhead
Agreements:
NR supports the following beam reporting considering L groups where L>=1 and each group refers to a Rx beam set (Alt1) or a UE antenna group (Alt2) depending on which alternative is adopted.
  For each group l, UE reports at least the following information:
    Information indicating group at least for some cases
      FFS: condition(s) to omit this parameter e.g. when L=1 or Nl=1
    Measurement quantities for Nl beam (s)
      Support L1 RSRP and CSI report (when CSI-RS is for CSI acquisition)
        FFS: the details of RSRP/CSI derivation and content
        FFS: Other reporting contents, e.g., RSRQ
        FFS: Configurability between L1 RSRP and CSI report
        FFS: whether or not to support differential L1 RSRP feedback
        FFS: How to select Nl beam(s) e.g max Nl beams in terms of received power being above a certain threshold or in terms of correlation less than a certain threshold
    Information indicating Nl DL Tx beam(s) when applicable
      FFS: the details on this information, e.g., CSI-RS resource IDs, antenna port index, a combination of antenna port index and a time index, sequence index, beam selection rules for assisting rank selection for MIMO tx, etc.
  This group based beam reporting is configurable per UE basis.
    This group based beam reporting can be turned off per UE basis e.g. when L=1 or Nl=1
      NOTE: No group identifier is reported when it is turned off
    FFS: how L is determined. e.g. by network configuration or UE selection or UE capability e.g. how many beams can be received simultaneously
    FFS: how is configured using the CSI framework to support multi-panel or multi-TRP transmission

## Slide 4: Proposal
Adopt at least Alt-2, i.e., UE reports information about TRP Tx Beam(s) per UE antenna group basis where UE antenna group refers to receive UE antenna panel or subarray.
  Consider the possibility of merging Alt-1 into Alt-2 if the benefit of Alt-1 can be observed
    System Level simulation is encouraged to identify whether any performance gain can be observed from Alt-1
  Identify scenarios where different Tx beams reported for different antenna groups can or cannot be received simultaneously at UE, and if needed any signaling support
  FFS how UE antenna group is captured in the specification
    E.g. group size, group reporting format