## Slide 1: Way forward on Uplink HARQ-ACK feedback
Ericsson, ..
R1-1706705
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, April 3 - 7, 2017
Agenda item 7.2.6.3

## Slide 2: Background
During RAN1#88bis, agreements on PUSCH HARQ feedback are achieved as follows:
For the purpose of evaluations of HARQ-ACK feedback for UE power saving:
  At least the following two options are considered for HARQ-ACK feedback channel:
    Option 1: One HARQ-ACK feedback channel for multiple UE PUSCHs in one transmission.
    Option 2: One HARQ-ACK feedback channel for a single UE PUSCH in one transmission
  Detailed design on HARQ-feedback channel FFS among at least the following options:
    PHICH-like channel.
    MPDCCH with reduced DCI size(s)
    MPDCCH with existing DCI size(s)
  Early termination of PUSCH transmission and/or MPDCCH monitoring are considered.
    The detailed solutions can be different for HD-FDD and FD-FDD/TDD.

## Slide 3: Proposal
  To evaluate PUSCH HARQ feedback the following assumptions are proposed:
    Metrics for evaluating performance:
      Other metrics are not precluded
      See next slides for detailed assumptions on power efficiency evaluations
    Assumptions for evaluating performance:
      Other assumptions important for achieved performance such as use of cross-subframe channel estimation should be declared.
Parameter | Value
BS TX antenna configuration | 2 Tx
BS power | 43 dBm per TX port
System BW | 10 MHz
Band | Band 8 (900 MHz)
Channel model | ETU
Doppler spread | 1 Hz
Frequency error | ±30 Hz
UE RX antenna configuration | 1 Rx
UE NF | 9 dB
Coupling loss | 144, 154, 164 dB
Performance Metric | Unit
Power efficiency | % (reduced power consumption)
BLER | %
False detection rate (Nack to Ack, DTX to Ack) | % (expressed as percentage of false detection events)
UE complexity | % (expressed as increase in complexity compared to Cat M1 Rel-13)
UL, DL overhead | Used REs for completing a transmission.

## Slide 4: Proposal Power efficiency
Device power consumption model:
The UE power consumption should be evaluated for the uplink transmission of 200 bytes (on top of PDCP).
  Power consumption for light sleep between search spaces, for MPDCCH reception and for PUSCH transmission should be taken into account.
  The targeted initial and residual BLER for the MPDCCH and PUSCH transmissions should be declared.
Operating mode | Power [units/ms] | Notes
Transmit | 500 | RF and baseband circuitry
Receive | 100 | RF and baseband circuitry
Light sleep | 1 | Corresponds to maintaining accurate timing by keeping RF frequency reference active.