## Slide 1
3GPP TSG RAN WG1 Meeting #88bis R1-1706730
Spokane, USA, April 3rd -7th, 2017
Agenda item: 8.1.2.3.3
WF on Schemes of Partial Channel Reciprocity
Huawei, HiSilicon, MediaTek, […]

## Slide 2: Background
The following agreements were achieved in RAN1 88
Update the RAN1 Jan. Ad hoc agreements as follows;
  Study the following DL CSI feedback for different degree of channel reciprocity,
    For full channel reciprocity
      Explicit interference feedback: e.g., Interference covariance matrix, diagonal elements of interference covariance matrix
      Implicit interference feedback: e.g., Interference PMI feedback
      Explicit channel feedback: e.g., CSI of multiple TRPs
    For partial channel reciprocity (e.g., more Rx ports than Tx ports at UE)
      Partial CSI feedback for eNB to acquire full CSI
    Non-PMI feedback (legacy: eNB send beamformed RS, and UE report RI/CQI)
      CSI contains RI and CQI
      FFS how RI and CQI are derived
        E.g., RI and CQI depend on a PMI which is selected from a defined codebook or a configured codebook subset
        UE may also calculate RI and CQI directly with estimated channel without assuming PMI from any predefined codebook, FFS spec impact
  Study whether or not to support CSI-RS and SRS transmission in the same slot (e.g., for fast CSI acquisition)
    Study if a limitation on the number of SRS and/or CSI-RS ports due to UE complexity, slot duration of different numerology are needed.

## Slide 3: Proposal
For the case of partial channel reciprocity (i.e., less Tx ports than Rx ports at UE), the following candidate schemes should be evaluated and compared based on the simulation assumption in the appendix
  Scheme 1: Partial CSI feedback
    Partial CSI is the information of the partial DL channel (e.g. partial DL channel vector/matrix or partial DL channel covariance matrix) which has no symmetric UL transmission due to no Tx ports corresponding to the Rx ports at UE
  Scheme 2: Non-PMI feedback
  Scheme 3: CSI feedback with beamed CSI-RS including CQI, RI and PMI
    Precoder for beamed CSI-RS is determined from CSI available at base station from SRS transmission
    PMI could be for a linear combination codebook
  Scheme 4: Joint usage of the above schemes

## Slide 4: Appendix
Parameters | Values
Duplex mode | TDD
Carrier frequency | 2GHz
Simulation bandwidth | 10MHz
Channel model | 3D UMI / UMA
BS antenna configuration | (M, N, P, Mg, Ng) = (8, 8, 2, 1, 1); (dH, dV) = (0.8, 0.5)λ
BS TXRU mapping | (MTXRU, NTXRU, P, Mg, Ng) = (2, 4, 2, 1, 1), (1, 4, 2, 1, 1)
UE antenna configuration | 1T2R, 2T4R, Cross-polarized with 0, 90deg
UE receiver noise figure | 9dB
UE antenna gain | Follow TR 36.873
Traffic model | Non-Full buffer, FTP model 1, 0.5MB packet size
UE distribution | 80% Indoor, 20% Outdoor
Scheduler | PF
HARQ scheme | Maximum 4 retransmissions
UE receiver type | MMSE-IRC
Channel estimation | Ideal / non-ideal
MIMO mode | MU-MIMO with rank adaptation