## Slide 1: WF on RS for time and frequency tracking and the evaluation assumptions
MediaTek, Samsung, Huawei, HiSilicon, ZTE, ZTE Microelectronics, Qualcomm, Ericsson, [Intel]
3GPP TSG RAN WG1 #88 bis
Spokane, USA, 3th – 7th April 2017
Agenda item: 8.1.2.4.6
R1-1706800

## Slide 2: Proposals
The RS(s) for fine time and frequency (T/F-) tracking should consider
  Whether T and F tracking use independent RS(s) respectively, or same RS
  The number of antenna ports for the RS(s)
  Whether already existing RS(s) used for other purposes can be used also for T and/or F tracking
  Whether the RS(s) are periodic or aperiodic
  Whether RS bandwidth and/or periodicity is configurable
    If it is configurable, the approach can be, e.g. by RRC, SIB , MIB,…
    Study the need of additionally scheduled to help UE from long CDRX wakeup
The RS supports the multi-beam operation
  At least 2 RS repetitions in the same TX beam within a given time duration is supported (e.g. RS in two OFDM symbols in the same slot)
The RS(s) also support delay spread estimation and Doppler spread estimation

## Slide 3: Proposals for evaluation assumptions
Transmission scheme
  Specify the interested transmission scheme
    For example, close loop or semi-open loop by RB level precoder cycling, one layer or two layers, fixed MCS
Example scenarios for evaluation
  high spectral efficiency with low speed
  high speed
  Low and high frequency band (e.g. 4 and 30GHz)
  Small and large number of TXRUs (e.g. 2 and 32)
  Scenario 1 and 2 are listed in coming slides, other not precluded
Location of reference signals
  PDSCH DMRS, CSI-RS and RS for time/frequency tracking should be indicated in order to properly calculate the coding rate, and to avoid collision between reference signals
Performance metric
  CDF of frequency/time tracking performances
  Frequency tracking trajectory comparison with the theoretical Doppler frequency change
  BLER trajectory or ACK/NAK trajectory
  Throughput statistics
  Others are not precluded

## Slide 4: Proposals for evaluation assumptions
Other parameters
  Specify the carrier frequency, subcarrier spacing, etc.
Channel model
  E.g. TDL, CDL defined in 38.901
  E.g. High speed train model defined in 36.101

## Slide 5: Proposals for evaluation assumptions
Scenario 1 for having initial time and frequency error (single TP, single panel)
  Fixed time offset= 1/x of CP length, frequency offset= 0.1ppm, Doppler spread= y [Hz], Delay spread= z [ns] per carrier frequency
    x , y, and z can be determined by companies
  For example, 4TX/8TX, 2RX/4RX

## Slide 6: Proposals for evaluation assumptions
Scenario 2 for high speed (single TP, single panel)
  Modify 36.101 B.3 high speed train scenario for up to 500km/hr and Fd=1850Hz
  For example, 4TX/8TX, 2RX/4RX
Carrier freq
2.7GHz
Ds
500m
Dmin
5m
velocity
350km/hr
fd
875Hz
Carrier freq
4GHz
Ds
1000m
Dmin
50m
velocity
500km/hr
fd
1850Hz
Figure B.3-1: Doppler shift trajectory in 36.101

## Slide 7: An example of tracking requirements
  The tracking signal performance requirement can be provided for example by the following table
Processing gain (dB)
Time delay
Range (fraction of S)
Drift between updates (Ts)
Granularity (Ts)
Processing gain (dB)
Frequency offset
transmission gap (S)
Drift between updates (Fs)
Processing gain (dB)
Delay/Doppler spread
transmission gap (S)
Tracking target
Tracking requirements
Note:
S: OFDM symbol time duration
Ts: sample time
Fs: subcarrier spacing
Processing gain: number of RS in one update (to ensure sufficient noise suppression)