## Slide 1: WF on Other System Information delivery
MediaTek, CATT, Intel, InterDigital, Nokia, NTT DoCoMo
R1-1706802
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, 3rd - 7th April 2017
Agenda Item: 8.1.1.2.2

## Slide 2: Background
Agreements in TR38.804:
  The other SI may either be broadcast, or provisioned in a dedicated manner, either triggered by the network or upon request from the UE.
  The other SI may be broadcast at configurable periodicity and for certain duration. It is network decision whether the other SI is broadcast or delivered through dedicated UE specific RRC signaling.

## Slide 3: Proposals
The broadcast delivery of other system information (OSI) is supported by NR-PDSCH transmission. The scheduling information of broadcast NR-PDSCH is considered to be carried by the following option(s):
    Option 1: Common NR-PDCCH
    Option 2: Remaining minimum system information
    Other options are not precluded
  FFS: Maximum TBS for OSI.