## Slide 1
3GPP TSG RAN WG1 Meeting #88bis R1-1706829
Spokane, USA, 3rd - 7th April 2017
Agenda item: 8.1.1.3
WF on Paging
Huawei, HiSilicon

## Slide 2: Background
Some agreements were achieved for paging :
For paging in multi-beam operation, support beam sweeping for paging, and study the following methods:
  Alt-1: Multiplexing paging with SS blocks
    FFS: Details of paging
  Alt-2: Adding another round of beam sweeping for paging
    Note: Another round of beam sweeping is different from the beam sweeping of SS burst set
  Other alternatives are not precluded
  Companies report their assumption for paging
Support the paging channel design at least for RRC idle mode as follows:
  Paging message is scheduled by DCI carried by NR-PDCCH and is transmitted in the associated NR-PDSCH
  FFS:
    Paging indication triggers UE beam reporting (if supported)
      Opt-1: paging indication is in DCI
      Opt-2: paging indication is in non-scheduled physical channel
    How to indicate SI update if it is supported in paging
Companies are encouraged to provide their views on
  Definitions of paging occasion and paging periodicity
  Content and payload of paging message

## Slide 3: Proposal
The search space of NR-PDCCH addressing the paging message can be configured by gNB
  FFS detailed signaling mechanisms