## Slide 1: WF on Conflict Free UE-to-NW Relaying
Intel, ITRI, Sony
3GPP TSG RAN WG1 Meeting #89 R1-1709405
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item - 6.2.9.2.3.1

## Slide 2: Background
In case either Remote UE or Relay UE transmission is not controlled by eNB, there is a probability that SL reception and transmission as well as UL transmission at Relay UE may collide
It is necessary to consider enhancements to resource allocation in order to avoid these conflicts

## Slide 3: Proposal
In case of bidirectional relaying, mechanisms to avoid collisions of SL TX/RX and UL TX at Relay UE are supported
  At least Relay UE/eNB control of Remote UE transmission resource is supported
  FFS how to coordinate SL TX/RX and UL TX of Relay UE in eNB controlled and Relay UE assisted operation
  FFS whether to support simultaneous TX in SL and UL