## Slide 1: On SS burst composition
Nokia
3GPP TSG RAN WG1 Meeting #88bis
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda: 7.1.1.1.2
R1-1709489

## Slide 2: Background
In RAN1#88 following agreement was made
For set of possible SS block time locations, further evaluation till next meeting by considering at least the following:
  Whether or not a SS block comprises of consecutive symbols and whether or not SS&PBCH in the same or different slots
  Number of symbols per SS block
  Whether or not to map across slot boundary(ies)
  Whether or not to skip symbol(s) within a slot or a slot set
  Contents of an SS block (note: the contents of an SS block may be further discussed during this meeting)
How SS blocks are arranged within a burst set, & the # of SS blocks per burst/burst set

## Slide 3: Proposal
For the possible SS block time locations following mapping is followed:
  For sub-carriers spacing of 15kHz, 30kHz and 120kHz , two possible SS block time locations are mapped to one slot of 14 symbols
  For sub-carriers spacing of 240kHz, five possible SS blocks time locations are mapped to one duration of 28 symbols
  In the mapping following requirements are met
    At least 2 symbols are preserved from the beginning from the SS burst for DL control
    At least 2 symbols are preserved at the end of the SS burst for e.g. guard period and UL control
    SS block does not cross the slot (of 7 symbols) boundary