## Slide 1: WF on Indication Method for Half Radio Frame Interval
LG Electronics, ZTE, InterDigital
R1-1714636
3GPP TSG RAN WG1 Meeting RAN1 #90
Prague, Czech Republic 21st – 25th August 2017
Agenda item: 6.1.1.2.2

## Slide 2: Background
Agreement : (RAN1 NRAH#2)
  Working assumption: 3 bits of SS block index are carried by changing the DMRS sequence within each 5ms period
  It can be further considered to limit the number of bits carried in this way to 2 if carrying 3 bits is shown to cause problems
  FFS: details of scrambling of the PBCH which may or may not carry a part of timing information
  FFS: 5 ms half radio frame interval indication
  Remaining bits of the timing information are carried explicitly in the NR-PBCH payload

## Slide 3: Motivation
The definition of PBCH TTI is that contents of PBCH is not changed within PBCH TTI.
  Hence, it is right design way that the indication of 1bit for half radio frame is not contained in MIB.
If the indication of 1 bit for half radio frame is contained in MIB, it is impossible to operate soft combining of 16 times within 80ms.
As one of design way, it can be considered that the indication of 1 bit for half radio frame indication is carried by PBCH-DMRS.
  This method has an advantage of providing soft combining between two PBCH data within 10ms radio frame without increasing blind decoding complexity in UE side.

## Slide 4: Proposal
Half Radio Frame Interval is indicated by PBCH-DMRS.
One solution should be selected among following alternative solutions:
  Alt.1: PBCH-DMRS sequence initialization
  Alt.2: PBCH-DMRS frequency shift
  Alt.3: PBCH-DMRS mapping order