## Slide 1: WF on Extension of Block Length for Base Graph #2
Ericsson, LG, CATT, Qualcomm
R1-1714687
3GPP TSG RAN WG1 Meeting #90
Prague, P.R. Czechia 21th – 25th August 2017
Agenda item 6.1.4.1.6

## Slide 2: Background
Agreement: (RAN1 NR AdHoc #2)
  Base graph #1 is used for the initial transmission and subsequent re-transmissions of the same TB when
    CBS > X or code rate of the initial transmission > Y
  Base graph #2 is used for the initial transmission and subsequent re-transmissions of the same TB when
    CBS <= X and code rate of the initial transmission <= Y
  Working assumption : X = 2560 and Y = 0.67
  FFS after PCM decisions if X can be extended to 3840 and/or Y can be extended to 0.75

## Slide 3: Discussion (1)
For and
  BG2 performs slightly better than BG1 at BLER
  BG1 performs slightly better than BG2 at BLER
By extending X to 3840, the decoding complexity in the region is reduced by more than 60%

## Slide 4: Discussion (2)
For and
  BG2 performs slightly better than BG1 at BLER
  BG1 performs significantly better than BG2 at BLER
The small performance improvement at BLER is not worth the larger loss at BLER

## Slide 5: Proposal
Change the working assumption X = 2560 and Y = 0.67 to X = 3840 and Y = 0.67