## Slide 1: WF on UL HARQ-ACK feedback enhancement
ZTE, Huawei, HiSilicon, Intel, Ericsson, Lenovo, MotoM, [Qualcomm], …
3GPP TSG RAN WG1 Meeting #90
Prague, Czechia, 21st – 25th August 2017
Agenda item 5.2.6.3
R1-1714747

## Slide 2
Background
  PUSCH tranmission schemes
    Scheme 1:To achieve target BLER by single transmission
    Scheme 2:To achieve target BLER by multiple PUSCH transmissions triggered by MPDCCH
    Scheme 3:To achieve target BLER by scheduling single transmission but early PUSCH termination is allowed if HARQ-ACK carried by MPDDCH is detected

## Slide 3
Background
  Simulation results (simulation assumptions refer to appendix)
  Note: The target BLER of MPDCCH is assumed to be 1%. The target BLER of PUSCH is assumed to be 10% for 154 dB MCL and 30% for 164 dB MCL.
 | Average Power Consumption |  | Average PUSCH Overhead |  | Average MPDCCH Overhead | 
 | Evaluation results for scenario 1 |  |  |  |  | 
Scheme 1 | 6.24×105 | 100% | 1024 | 100% | 4.0047 | 100%
Scheme 2 | 3.5394×105 | -43.28% | 577.7212 | -43.58% | 9.0378 | +125.68%
Scheme 3 | 3.5814×105 | -42.61% | 584.8501 | -42.89% | 7.3898 | +84.53%
 | Evaluation results for scenario 2 |  |  |  |  | 
Scheme 1 | 6.24×105 | 100% | 1024 | 100% | 4.0047 | 100%
Scheme 2 | 3.2281×105 | -48.27% | 516.3317 | -49.58% | 16.1547 | +303.39%
Scheme 3 | 3.2686×105 | -47.62% | 523.2513 | -48.90% | 7.6218 | +90.32%
 | Evaluation results for scenario 3 |  |  |  |  | 
Scheme 1 | 1.248×106 | 100% | 2048 | 100% | 64.347 | 100%
Scheme 2 | 9.5733×105 | -23.29% | 1562.6 | -23.7% | 196.387 | +205.2%
Scheme 3 | 9.7891×105 | -21.56% | 1598.9 | -21.93% | 97.5392 | +51.58%

## Slide 4
Observations
  Observation 1: Average power consumption and PUSCH overhead of scheme 3 are lower than those of scheme 1.
    Average power consumption and average PUSCH overhead of scheme 2 and scheme 3 are similar.
  Observation 2: Average MPDCCH overhead of scheme 3 is lower than that of scheme 2.

## Slide 5
Proposal
  Explicit HARQ-ACK feedback channel is supported.
    Explicit HARQ-ACK feedback can be used to
      terminate PUSCH transmission at least in FD-FDD and TDD
      potentially terminate MPDCCH monitoring before going to sleep (up to RAN2)
    FFS search space for explicit HARQ-ACK feedback

## Slide 6
Appendix (1)
  Simulation scenario 1 (154 dB MCL):
    936-bit TBS is assumed.
    For scheme 1, number of repetitions is 1024.
    For scheme 2, number of repetitions for each transmission is 256 and search space interval is 320.
    For scheme 3, interval of adjacent two PUSCH detections is 256 subframes. 4 subframes are reserved for eNB’s PUSCH decoding and UE’s MPDCCH decoding.
    Rmax is assumed to 32 subframes.

## Slide 7
Appendix (2)
  Simulation scenario 2 (154 dB MCL):
    936-bit TBS is assumed.
    For scheme 1, number of repetitions is 1024.
    For scheme 2, number of repetitions for each transmission is 128 and search space interval is 160.
    For scheme 3, interval of adjacent two PUSCH detections is 128 subframes. 4 subframes are reserved for eNB’s PUSCH decoding and UE’s MPDCCH decoding.
    Rmax is assumed to 32 subframes.

## Slide 8
Appendix (3)
  Simulation scenario 3 (164 dB MCL):
    328-bit TBS is assumed.
    For scheme 1, number of repetitions is 2048.
    For scheme 2, number of repetitions for each transmission is 512 and search space interval is 640.
    For scheme 3, interval of adjacent two PUSCH detections is 512 subframes. 4 subframes are reserved for eNB’s PUSCH decoding and UE’s MPDCCH decoding.
    Rmax is assumed to 64 subframes.