## Slide 1: WF on UE self-interference handling
China Unicom, Orange, vivo, OPPO
3GPP TSG RAN WG1 meeting #90 R1-1714837
Prague, Czech Republic, 21 – 25 August, 2017
Agenda item: 6.1.6

## Slide 2: Background
Harmonic interference has been identified as a issue in some specific band combinations and followings were agreed in RAN1 NR adhoc#2
  Agreements:
    RAN1 to continue study the solution(s) to mitigate UE self-interference due to the simultaneous transmission and reception at the same time
      Note: the issue is particular applicable for specific band combination(s) (e.g. harmonics related issues)
      Note: the issue can be addressed if UE is not mandated to transmit on one carrier (F1) and receive on another carrier (F2) at the same time
    Send an LS to RAN4 regarding the above agreements , which is approved in R1-1711872

## Slide 3: Proposal
RAN1 should investigate the potential FDM approaches for harmonic interference handling between a pair of UL (F1) and DL (F2) carriers
  One example for FDM approach: UE simultaneous transmission on UL F1 and reception on DL F2 is assumed, i.e. full duplex, but the transmission on the part of DL F2 impacted by harmonic interference due to UE simultaneous transmission on UL F1 is avoided