## Slide 1
LG Electronics, Ericsson, InterDigital, Samsung, ZTE, Nokia, Nokia Shanghai Bell, KT, Huawei
R1-1714875
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21th – 25th August 2017Agenda Item: 6.1.2.3.4
WF on PT-RS frequency density table

## Slide 2: Background I
RS overhead comparisons between two types of PT-RS frequency density tables
  Tables A and B refer to PT-RS frequency density tables presented in [1] and [2], respectively.
  The number of PT-RS subcarriers for Table A is under bounded by that for Table B regardless of subcarrier spacings when the number of PRBs is less than 64.
  For example of 7 PRBs, the RS overheads of Table A and B are 4.76% and 8.33%, respectively. For the number of PT-RS ports being 4, their RS overheads are 19% and 33.3%, which indicates that Table B leads to additional 14.3% spectral efficient loss than Table A.
  [1] R1-1714622 On UL PT-RS design, LG Electronics. [2] R1-1711047 On DL PTRS design, Ericsson.

## Slide 3: Background II
Spectral efficiency for 60/120kHz, 64PRBs, and 256QAM(3/4)
  For PT-RS subcarriers of 8, there is 1.8dB performance loss for PN model in [6], while the other PN models produce slight performance loss.
  In order to avoid to determine the number of PT-RS subcarriers according to PN models, it is better to choose the number of PT-RS subcarriers of 16 for 64PRBs.
1.8dB

## Slide 4: Proposal
PT-RS frequency density table
  The listed BW thresholds are only for the predefined table.
  As agreed before, the BW thresholds can be RRC configured by gNB.
Scheduled BW | Frequency density
NRB < 3 | No PT-RS
3≤ NRB < 5 | 1
5≤ NRB < 16 | 4/NRB
16≤ NRB | 1/4
The distance between RBs containing PT-RS is equal, see example on the following page.

## Slide 5: Appendix
Location of RB including PT-RS
  The distance between adjacent RBs including PT-RS can be determined by one of the set {1, 2, 4} RBs.
  For with the number of PT-RS subcarriers being 4, it can be illustrated as