## Slide 1: WF on codeword mapping
MediaTek, ZTE, Vivvo
3GPP TSG RAN WG1 #90 R1-1714879
Prague, Czech, August 21st – 25th 2017
Agenda item: 6.1.2.1.1

## Slide 2: Background
Working assumption:
In NR, support at least the following mapping order for modulated symbol stream to the allocated resource for DL data channel
  First across layers associated with the codeword, then across subcarriers (frequency) and then across OFDM symbols (time)
  FFS whether the resource is associated with a CW or with a CB group
FFS other schemes (e.g., Layer Time Frequency, Time Frequency Layer, Frequency Layer Time)
  If so, details of configuration signalling, e.g. RRC, DCI
  Companies are strongly encouraged to perform evaluations especially for high-speed scenarios, and interference limited/varying scenarios
Notes: Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.

## Slide 3: Proposal
For the coordinated transmission with single PDSCH, the following CW to resource mapping should be supported:
  In case of single CW:
    Layer group 1  Frequency  Time  Layer group 2  Frequency  Time