## Slide 1: WF on multiple starting positions in a subframe for uplink in FeLAA
Huawei, HiSilicon, [Nokia],[…]
3GPP TSG RAN WG1 #90 R1-1714904 Prague, Czech Republic
21st – 25th August, 2017
Agenda item: 5.2.2.2
Document for decision

## Slide 2: Background
In the RAN1 meeting #89, the following agreements were achieved:
  UL partial subframe transmission starting at symbol #7 is supported with both following modes Mode 1 and Mode 2
  Mode 1. The UE may start at a Rel-14 starting point or at symbol #7 depending on e.g. the outcome of LBT
    The TBS is determined as for the full subframe regardless of the starting point (i.e. no TBS scaling)
    FFS: channel access within shared COT
    FFS: how to indicate to which UL subframes this applies
    FFS: UCI mapping, if supported
  Mode 2. The UL grant indicates starting position at number #7
    FFS: additional starting points between symbols #7 and #8
    The TB(s) is rate matched into the second slot
    TBS Scaling is used similarly as in FS2
      FFS: TBS scaling details
    FFS: UCI mapping, if supported

## Slide 3: Proposal
UL subframes which are allowed to apply Mode 1 transmission should be indicated to UE.
Indicating schemes for UL subframes which are allowed to apply Mode 1 transmission
  Option 1: RRC configuration in the means of subframes window
  Option 2: MAC-CE configuration for the permitted subframes
  Option 3: Be dynamically indicated in the UL grant
  FFS: others