## Slide 1: WF on supported use case for CA
Huawei, HiSilicon, OPPO
3GPP TSG RAN WG1 Meeting #90 R1-1714934
Prague, Czech Republic, August 21-25, 2017
Agenda item – 5.2.3.1

## Slide 2: Background
At the RAN1#89 meeting, the following agreements were reached for CA of Rel-15 sidelink:
For RAN1, 3 use cases are considered for CA (Note that all use cases may not necessarily be supported):
  (first case) Parallel transmission of MAC PDUs (‘parallel’ means at the same or different transmission time, but on different carriers). The MAC PDU payloads are different.
  (second case) Parallel transmission of replicated copies of the same packet (‘parallel’ means at the same or different transmission time, but on different carriers)
    FFS at which layer replication is done
  (third case) Capacity improvements from the receiver perspective
    Note: From the receiver’s perspective, simultaneous reception over multiple carriers is assumed. From a transmitter’s perspective, transmission occurs over a subset of the available carriers
    For example, capacity could be increased a UE transmits on a single carrier (which can be different for each UE), but receives over all carriers

## Slide 3: Proposal
For the three CA use cases identified in RAN1#89
  First and third use case are prioritized in RAN1.
  For the second case, packet duplication can be done at higher layers (up to RAN2 to decide).
Send an LS to RAN2 to inform them of the decision.