## Slide 1: WF on resource selection for CA in V2X
CATT, OPPO, …
3GPP TSG RAN WG1 Meeting #90 R1-1714943
Prague, Czechia, 21st – 25th August, 2017
Agenda Item: 5.2.3.1.2

## Slide 2: Background
In RAN1 #89 meeting, the following agreements were achieved
  For RAN1, 3 use cases are considered for CA (Note that all use cases may not necessarily be supported):
    (Use case 1)Parallel transmission of MAC PDUs (‘parallel’ means at the same or different transmission time, but on different carriers). The MAC PDU payloads are different.
    (Use case 2)Parallel transmission of replicated copies of the same packet (‘parallel’ means at the same or different transmission time, but on different carriers)
      FFS at which layer replication is done
    (Use case 3)Capacity improvements from the receiver perspective
      Note: From the receiver’s perspective, simultaneous reception over multiple carriers is assumed. From a transmitter’s perspective, transmission occurs over a subset of the available carriers
      For example, capacity could be increased a UE transmits on a single carrier (which can be different for each UE), but receives over all carriers

## Slide 3: Observations
For use case 1 and use case 2, if the intra-band CA is applied, the UE transmitting multiple packets in multiple carriers drops too many reception opportunities due to half-duplex impact.

## Slide 4: Proposals
The resource selection enhancements should be supported in order to reduce half-duplex impact caused by the parallel transmissions by one Tx UE from multiple carriers.
  Enhancement details FFS