## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-1715035
Prague, Czech Republic, 21-25 August 2017
Agenda Item: 6.1.1.3
WF on paging mechanism
Huawei, HiSilicon, …

## Slide 2: Background
Agreements in RAN1#88:
Support the paging channel design at least for RRC idle mode as follows:
  Paging message is scheduled by DCI carried by NR-PDCCH and is transmitted in the associated NR-PDSCH
  FFS:
    Paging indication triggers UE beam reporting (if supported)
      Opt-1: paging indication is in DCI
      Opt-2: paging indication is in non-scheduled physical channel
    How to indicate SI update if it is supported in paging

## Slide 3: Background
Maximum number of SS blocks is 64.
Subcarrier spacing is 120 KHz, the total symbols of each system frame are 1120.
20ms default SS burst set periodicity => 128 symbols for SS block transmission per 10ms frame on average
Paging capacity as LTE: each frame has 4 POs and each PO occupies two symbols: one for PDCCH and one for PDSCH. Paging will need symbols.
Considering TDM of paging and SS block
  512 + 128 = 640 symbols for paging and SS block
As a result, 640/1120=57% symbols will contain beam sweeping for paging and SS block
  Note: RMSI and RACH also need beam sweeping

## Slide 4: Proposal
The paging mechanism for NR Rel-15 is selected from the following options
  Option 1: LTE paging mechanism where up to 16 UEs can be paged in one PO
  Option 2: LTE paging mechanism where more than 16 UEs can be paged in one PO
  Option 3: Paging indication triggers UE beam reporting
  Note: combination of the above techniques is not precluded
  Other options are not precluded
  Note: Other techniques can be applied to reduce the overhead
    E.g., Compressed UE ID
    E.g., UL mobility to reduce the number of sweep beams for paging transmission