## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-1715036
Prague, Czech Republic, 21-25 August 2017
Agenda Item: 6.1.1.2.2
WF on SS block time index indication
Huawei, HiSilicon, …

## Slide 2: Background
In the RAN1 AH meeting the working assumption and agreements on DMRS sequence design and RE mapping for NR-PBCH were achieved as follows:
Working assumption:3 bits of SS block index are carried by changing the DMRS sequence within each 5ms period
  It can be further considered to limit the number of bits carried in this way to 2 if carrying 3 bits is shown to cause problems
FFS: details of scrambling of the PBCH which may or may not carry a part of timing information
FFS: 5 ms half radio frame interval indication
Remaining bits of the timing information are carried explicitly in the NR-PBCH payload

## Slide 3: Proposal
NR should define an SS burst composed of a subset of consecutive slots containing SS blocks
  SS block time index that is specific to each SS block within an SS burst, and an SS burst index that is specific to each SS burst within an SS burst set.
  SS burst index is common across SS blocks in each SS burst.
  The SS blocks within an SS burst are indicated by DMRS in ascending order.
  The SS bursts within an SS burst set are indicated by NR-PBCH payload in ascending order.
  The PBCH content of different SS blocks within an SS burst is the same.