## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-1715097
Prague, Czechia, 21th – 25th August 2017
Agenda item: 6.1.2.2.6
WF on UE assistance information for UL Beam Management
MediaTek, Samsung, Intel, Huawei, HiSilicon, [ZTE]

## Slide 2: Background
Agreements in RAN1 88bis meeting:
  Study whether or not the UE to provide information to gNB to assist UL beam management without UE beam correspondence
    E.g., the amount of SRS resources that is needed to train UE Tx beams, based on DL beam management results if available

## Slide 3: Proposal
Support UE to provide information to gNB to assist UL beam management
  The information can be a number representing the amount of SRS resources required for UE Tx beam training
  FFS: signaling method
    E.g., capability signaling, or msg3, or dynamic signaling
  FFS: if and how to support the antenna structure with both omni-directional antenna panel and directional antenna panel
    whether the number of SRS resource should be reported per panel