## Slide 1: Way forward on scheduling request support in NR
Ericsson, NTT DOCOMO, Nokia, Nokia Shanghai Bell
R1-1715101
RAN1 #90
Prague, Czech Republic, 21-25 August 2017
Ag. 6.1.3.3.2

## Slide 2: Background
To complete the NR design it is essential to define the signaling for SR operation.
Relevant RAN2 agreements (from LS R1-1710211)
  “Agreements
    Multiple SR configurations can be configured to the UE and which SR configuration is used depends on the LCH that triggers the SR. The granularity of SR configuration for a logical channel is FFS.
    From RAN2 point of view a single bit SR with multiple SR configuration is sufficient to distinguish the “numerology/TTI length” of the logical channel that trigger the SR. RAN2 has not identified other use cases for which multibit SR is need with sufficient support.
    RAN2 does not see the need to convey buffer status information.
    Send LS to RAN1 to indicate to RAN1 that RAN2 doesn’t see the need to support multi-bit SR. “

## Slide 3: Proposal
The UE can be configured with more than 2 separate SR configurations.
Each SR configuration maps to one or more logical channels
  Details of mapping (including whether transmission profiles are used as part of mapping) are up to RAN2
If multiple SRs are triggered to be transmitted overlapping in time, the UE will only transmit the SR corresponding highest priority.
  Details on how to do the prioritization is up to RAN2 to decide
An SR can be configured with a periodicity of one OFDM symbol up to the largest periodicity supported in LTE (i.e. XX ms)
An SR can be configured with both short and long PUCCH (of different lengths)