## Slide 1: WF on UE assistance for PTRS port configuration for CP-OFDM
Huawei, HiSilicon, Intel, National Instruments, ZTE, LG Electronics, […]
3GPP TSG RAN WG1 Meeting #90 | R1-1715158
Prague, Czech Republic, 21-25 August 2017 | Agenda Item: 6.1.2.3.4

## Slide 2: Background
Phase tracking are targeting at the phase fluctuations, not only the initial phase
  Even if the initial phase are calibrated, the phase fluctuations on different TXRUs can still be very different, due to independent oscillator and/or multipliers
The agreed model of non-calibrated panel in TR38.802 only captures different initial phases
  “Phase offset of non-calibrated panel (either TRP or UE side) is modeled as a uniform distributed random variable between ().”
Whether gNB TXRUs share a common oscillator or not is know to gNB itself

## Slide 3: Background
Whether the TXRUs at a UE sharing a common oscillator or not is unknown to gNB if there is no indication from this UE.
Such information can help gNB to configure the number of PTRS ports and association between DMRS and PTRS (e.g., using one PTRS port if common oscillator and multiple PTRS ports otherwise), leading to reduced overhead and improved throughput.

## Slide 4: Background
Agreements in RAN1#89
  Study the benefits of configuring the number of PTRS ports for a UE, based on UE capability or UE report on
    Panels/TXRUs sharing a common oscillator or not, and/or
    Maximum number of independent oscillators at this UE, and/or
    Whether phase errors measured on PTRS ports are same or different
Agreements in RAN1#AH1706
  For PTRS for CP-OFDM, NR supports
    Information related to UE to facilitate PTRS port configuration
      FFS details, e.g., UE to report information (if so, details), or re-using UE information available for other purposes

## Slide 5: Proposal
To facilitate PTRS port configuration, support UE to report the number of PTRS ports desired by this UE
  Note: UE can derive this information from the number of UE TXRUs and whether they share an oscillator or RF chain