## Slide 1: WF on CSI feedback for NCJT
LG Electronics, Ericsson, Intel
Agenda item:
3GPP TSG RAN WG1 Meeting #90 R1-1715165
Prague, Czech Republic, 21st – 25th August 2017
Agenda item: 6.1.2.1.6

## Slide 2: Agreements

## Slide 3: Proposals
For NCJT, M NZP CSI-RS resources are configured for channel measurement, where the following CSI feedback is supported:
  For multiple PDCCH based NCJT,
    Reporting PMI/RI per CSI-RS resource
      RIi, PMIi for i-th CSI-RS resource is calculated assuming layers on all CSI-RS resources mutually interfere
    Reporting CQI per CW per CSI-RS resource
      CQIi for i-th CSI-RS resource is calculated assuming layers on all CSI-RS resources mutually interfere
  For single PDCCH based NCJT,
    Reporting PMI/RI per CSI-RS resource
      RIi, PMIi for i-th CSI-RS resource is calculated assuming layers on all CSI-RS resources mutually interfere
    FFS Reporting CQI per CW per CSI-RS resource or reporting CQI per CW
      CQI is calculated assuming layers on all CSI-RS resources mutually interfere
  FFS maximum value of M