## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-1715166
Prague, Czech Republic, 21-25 August 2017
Agenda item: 6.1.1.5.2
WF on CSI-RS configuration for C-DRX UE
Huawei, HiSilicon, Qualcomm, MediaTek

## Slide 2: Background
Following agreements on measurement based on CSI-RS for L3 mobility have been reached in RAN1 #NR Adhoc 2:
  Agreements:
  Following CSI-RS properties for RRM measurement for L3 mobility are supported in NR
    Configurable periodicity (as already agreed)
      {5, 10, 20, 40, [80, 160]} ms are supported
      This does not mean periodicity will be configured per CSI-RS resource
    Configurable transmission bandwidth (as already agreed)
      FFS candidate values
    Configurable measurement bandwidth (as already agreed) and frequency location
      At least minimum carrier bandwidth for each frequency band/range and at least one additional wider bandwidth for each SCS (e.g., maximum UE bandwidth) are supported
        FFS other candidate values for wider bandwidth for each SCS
      Measurement of CSI-RS in subband/bandwidth part which may or may not contain SS Blocks is supported
    Configurable parameters for sequence generation
    Configurable numerology
      For each frequency range, subcarrier spacing values applicable to data, CSI-RS for beam management and SS block in the frequency range are supported
    Association between CSI-RS for RRM measurement and SS block
      It is assumed that property of spatial QCL between SS block and CSI-RS for beam management will be reused
    Configurable CSI-RS time/frequency resource (as already agreed)
      CSI-RS design including RE mapping and density for beam management is assumed as baseline
      For Connected DRX UE, the CSI-RS configuration should consider the power consumption issues.

## Slide 3: Proposal
For C-DRX operation, CSI-RS for L3 mobility is configured only within C-DRX UE’s active time, if CSI-RS for L3 mobility is configured to the UE.
  active time is a period wherein UE is monitoring PDCCH (e.g. OnDuration)