## Slide 1: WF on RBs for mapping PTRS for CP-OFDM
Huawei, HiSilicon, Ericsson, […]
3GPP TSG RAN WG1 Meeting #90 | R1-17xxxxx
Prague, Czech Republic, 21-25 August 2017 | Agenda Item: 6.1.2.3.4

## Slide 2: Background
Proposal in R1-1711895
  For non-consecutive scheduling, RB(s) is/are selected for mapping PTRS based on relative index among the scheduled RBs
Agreements in RAN1#AH1706
  For PTRS for CP-OFDM, study further how to handle mapping PTRS in case of non-consecutive scheduling
    Alt 1: based on PRBs
    Alt 2: based on VRBs
    Other alternatives are not precluded
    Note: consecutive scheduling can be considered as a special case

## Slide 3: Background
Illustration from R1-1712241
  If the RBs for mapping PTRS are selected based on the absolute index, we will be at the risk of mapping PTRS to RBs which are not allocated to this UE and even higher overhead than the desired one. In addition, if the PTRS on RBs non-allocated to this UE are simply not mapped, in extreme cases, we may end up with no or much less PTRS in frequency domain, leading to reduced accuracy of phase tracking
  Propose to select RBs for mapping PTRS based on relative index among the allocated RBs. Such a translation (from absolute to relative index) can ensure PTRS not mapped to non-allocated RBs, keep the desired overhead, and more importantly provide uniformly distributed PTRS within the allocated RBs for better robustness against frequency-selective fading.

## Slide 4: Proposal
For non-consecutive scheduling, PTRS is mapped to every nth RB among the scheduled RBs only
  The value of n is determined using the same configured/predefined table as for contiguous resource allocation
    The number of scheduled RBs (NRB) in the table is interpreted as the actual number of scheduled RBs
  FFS on RB location offset in steps of one RB