## Slide 1: WF on PDCCH / PDSCH resource sharing
ZTE, Ericsson, Nokia, Intel, LGE, Interdigital, TCL, Samsung, CATT
3GPP TSG RAN WG1 #90
Prague, Czech Republic, 6.1.3.1.3
R1-1715224

## Slide 2: Background
Agreements from RAN1#90:
Agreements:
A UE can be configured by RRC signaling with one or more resource set(s)
  The UE shall assume that the scheduled PDSCH is rate-matched around the resource set(s) when the scheduled PDSCH overlaps
  FFS: exact configuration of a resource set including granularity.
Agreements:
A UE can be configured by UE-specific RRC signaling to identify resource set(s) for which the PDSCH may or may not be mapped based on the L1 signaling.
  For a scheduled PDSCH overlapping with given resource set(s), L1 signalling indicates whether the scheduled PDSCH is rate-matched around the resource set(s) or is mapped to the resources in the resource set(s).
  FFS: details of the L1 signaling
  FFS: exact configuration of a resource set including granularity

## Slide 3: Proposal
    At least the following is supported
      When the scheduled PDSCH overlaps with the PDCCH scheduling the PDSCH, the UE shall assume that the scheduled PDSCH is rate-matched around the PDCCH scheduling the PDSCH
        Other forms of resource sharing between PDCCH and PDSCH are not precluded