## Slide 1: WF on PBCH design
Qualcomm
3GPP TSG RAN WG1 Meeting #90b R1-1719020
Prague, CZ, 9th – 13st, October 2017
Agenda item: 7.1.1
Document for decision

## Slide 2: Below 6GHz
Dual numerologies for bands 5 and 66 only
  15kHz SSB, 18RB PBCH, 2 PBCH symbols
  30kHz SSB, 18RB PBCH, 2 PBCH symbols
For other bands with 5MHz min BW
  15kHz SSB, 18RB PBCH, 2 PBCH symbols
For other bands with 10MHz min BW
  30kHz SSB, 18RB PBCH, 2 PBCH symbols

## Slide 3: Above 6GHz
240kHz SSB, 16RB PBCH, 3 PBCH symbols
60
120
240
0 1 2 3 4 5 6 7 8 9 10 11 12 13
Current
60
120
240
0 1 2 3 4 5 6 7 8 9 10 11 12 13
Proposed

## Slide 4: Appendix

## Slide 5: Evaluation
56 PBCH payload (RAN1 #90b WA)
36 RBs for PBCH in total
SSS is not used in channel estimation
R1-1610959, WF on Updated Link Level Evaluation Assumptions for Initial Access in NR

## Slide 6: PBCH BLER: single cell
SNR = -6dB
Design | Doppler | SSB SCS = 15kHz |  | SSB SCS = 30kHz | 
 |  | 1 soft combine | 2 soft combines | 1 soft combine | 2 soft combines
36 RBs for PBCH | 3km/h | 11.837% | 0.397% | 5.472% | 0.054%
 | 120km/h | 12.629% | 0.449% | 5.637% | 0.054%
2 PBCH symbols (24 RBs) | 3km/h | 5.073% | 0.073% | 2.090% | 0.000%
 | 120km/h | 5.390% | 0.055% | 2.194% | 0.009%
Both proposed design and current design requires 2 soft-combining to achieve less than 1% PBCH BLER at -6dB

## Slide 7: PBCH BLER: multi-cell
SINR = -6dB, 3 cells (SIR1 = 0dB, SIR2 = -3dB)
  R1-1610959: “2 interfering TRPs (1st SIR = 0dB, 2nd SIR = -3dB; SIR is defined as the ratio of power between a reference cell and interfered cell) – timing arrival differences from TRPs are provided by each proponent: optional”
Design | Doppler | SSB SCS = 15kHz | 
 |  | 1 soft combine | 2 soft combines
36 RBs for PBCH | 3km/h | 13.688% | 0.893%
 | 120km/h | 14.449% | 0.975%
2 PBCH symbols (24 RBs) | 3km/h | 5.282% | 0.080%
 | 120km/h | 5.845% | 0.082%
Both proposed design and current design requires 2 soft-combining to achieve less than 1% PBCH BLER at -6dB