## Slide 1: WF on Beam Management
Samsung, CATT, Huawei, HiSilicon, NTT Docomo, MediaTek, Intel, OPPO, SpreadTrum, AT&T, InterDigital, CHTTL, KDDI, LG Electronics, Sony, China Unicom, Ericsson, VIVO, China Telecom, Qualcomm, National Instruments, Vodafone
R1-1719059
3GPP TSG RAN WG1 #90bis
Prague, Czech, 9 – 13 Oct 2017
Agenda item 7.2.2.3

## Slide 2: Proposals: Beam measurement and reporting
Proposal:
  Support Alt#1 for SSB: configuration of SSB resources within a resource setting for beam management. L1-RSRP measurement on those configured resources is reported.
  For non-grouping based beam reporting, support the following reports parameters:
    Maximal number of configured Tx beams for beam measurement: K equals 64
    Maximal number of configured Tx beams to be reported in one instance: N_max = 2, 4 where a subset of N (N<=N_max where N = 1, 2, 4) beams can be selected by the gNB and indicated to the UE (FFS signaling mechanism)
    Reporting differential L1-RSRP when multiple beams are reported in one reporting instance. Reference is the largest L1-RSRP in that reporting instance. FFS other reference for differential reporting.
      FFS applicable reporting channels and number of beams, and associated reporting contents
      FFS: the UE adjusts the L1-RSRP of multiple RS resources according to the power offset between them
    Bit-width: 7bit for L1-RSRP ranging from -140dBm to -44dBm with 1dB stepping size (analogous with LTE) and 4bit for differential L1-RSRP
      FFS stepping size of differential quantization

## Slide 3: Proposals: UL beam management
For UL beam management,
  NR supports gNB configuration of transmitting SRS with same Tx beam across multiple symbols via either of followings
    configuring one SRS resource spanning multiple symbols
    configuring UE to apply the same Tx beam across the SRS resources in a SRS resource set.
  UE can apply different Tx beams to different SRS resources if it is not configured to apply the same Tx beam across SRS resources in a SRS resource set, where the beams can be determined either (1) via a gNB-transparent way , or (2) via gNB indication.
  NR supports the gNB to configure the UE to apply same Tx power on SRS resources within a SRS resource set for UL beam management.
  After receiving the SRS, NR supports gNB to update the SRS resource within the SRS resource set for beam management by RRC.

## Slide 4: Proposals: Update the association of TCI state and DL RS
FFS from RAN1 NR AH3:
  Mechanisms to initialize/update the ID of a DL RS(s) in the RS Set used at least for spatial QCL purposes
    At least the following two mechanisms are FFS: (1) explicit signaling to the UE of the DL RS(s) ID and corresponding TCI state (2) implicit association of the DL RS ID(s) to a TCI state based on measurements by the UE.
    The mechanisms used for different RS types are FFS
Proposal
  Initialization/Update of the ID of a DL RS(s) in the RS Set used at least for spatial QCL purposes is done at least via explicit signalling. Support the following methods for the explicit signalling :
    RRC
    RRC + MAC-CE
  Implicit Update via “implicit association of the DL RS ID(s) to a TCI state based on measurements by the UE.” is FFS

## Slide 5: Proposals: Presence of TCI in DCI
Proposal: For the case when at least spatial QCL is configured/indicated, support higher-layer UE-specific configuration of whether or not TCI field is present in DL-related DCI
  Not present: No dynamic indication of QCL parameters for PDSCH is provided in DL-related DCI
    For PDSCH, UE applies higher-layer signalling of QCL parameters/indication for determining QCL parameters (details: FFS) except for the case of beam management without beam-related indication (ref:Annex) where no spatial QCL parameters are higher layer configured
  Present: Details on Slide 7.
  Proposed candidate solutions should consider
    Below and above 6GHz DL beam related operation with and without beam indication
    Downlink beam management with and without beam indication (ref Annex)
Note: this proposal does not apply to the case of beam management without beam-related indication (ref:Annex)

## Slide 6: Proposals: timing issue of beam indication for PDSCH
Proposal: For the case when at least spatial QCL is configured/indicated, NR supports the beam indication for PDSCH as follows, if TCI field is present:
  The TCI field is always present in the associated DCI for PDSCH scheduling irrespective of same-slot scheduling or cross-slot scheduling.
  If the scheduling offset < threshold K: PDSCH uses a pre-configured/pre-defined/rule-based spatial assumption (details: FFS)
    FFS: The other QCL parameters are still obtained from the N-bit TCI state field in the DCI.
    FFS: How to update pre-configured/pre-defined spatial assumption (if applicable)
    Threshold K can be based on UE capability only if multiple candidate values of K are supported.
  If the scheduling offset >= threshold K: PDSCH uses the beam (spatial QCL parameter) indicated by the N-bit TCI field in the assignment DCI.
Note: this proposal does not apply to the case of beam management without beam-related indication (ref: Annex)

## Slide 7: Annex

## Slide 8: Background: Beam management without beam indication
Agreement (RAN1 #86b)
  For downlink, NR supports beam management with and without beam-related indication
Agreement (RAN1 #87)
  NR supports with and without a downlink indication to derive QCL assumption for assisting UE-side beamforming for downlink control channel reception
Agreement (RAN1 NR Ad Hoc #1)
  For downlink, NR supports CSI-RS reception with and without beam-related indication
Agreement (RAN1 #89)
  Support spatial QCL assumption between antenna port(s) within a CSI-RS resource(s) and antenna port of an SS Block (or SS block time index) of a cell
    The other QCL parameters not precluded
    FFS: indication either explicit or implicit or configurable or a default
    Note: default assumption may be no QCL