## Slide 1: WF on multiple ending positions in a UL subframe in FeLAA
CableLabs, Broadcom, Comcast, HPE,
Charter Communications, Brocade, Blackberry
3GPP TSG RAN WG1 Meeting #91 R1- 1721074
Reno, Nevada, 27th Nov – 1st Dec 2017
Agenda item: 6.2.2.1

## Slide 2: Background
Partial SFs ending at symbol 3 can be used to transmit a significant amount of data due to the very high SINR observed in typical 5GHz small cell configurations.
Even BE traffic with large IP packets can have smaller TBs due to segmentation and (re)assembly at the RLC and MAC. So, a large number of such smaller packets can be carried in an UL end partial SF ending at symbol #3.
SFs ending at symbol #3 and symbol #10 will also increase channel utilization and spectral efficiency of LAA. The LAA eNB or UE can win the channel at any time instant. However, COTs are in integer multiples of 1ms and UL transmissions can only start at 0.5ms boundaries. So, LAA can waste up to 0.5ms of transmission opportunity. Definition of a partial SF ending at symbol #3 or symbol #10, will enable LAA to utilize an additional 3 symbols of transmission every time it wins the COT at or after the end of symbol #3 and before the end of symbol #6 or after the end of symbol #10 and before the end of the subframe.
Increase in the number of ending positions in UL subframes will reduce the chances of the UE having to transmit lower priority data or padding in order align the end of the SF to the available choices
Partial SFs ending at symbol #3 and symbol #10 have already been defined for the LAA DL, much for the same reasons as discussed above. So, it is only natural to define them for LAA UL too, especially since defining such subframes does not introduce any significant implementation complexity.

## Slide 3: Proposal
UL subframes ending at the end of symbol 3 and symbol 10 respectively shall be supported. (full subframe symbol numerology: 0, 13)