## Slide 1: WF on Power Saving Signal Configuration for DL Channel in NB-IoT
Ericsson, …
3GPP TSG RAN WG1 Meeting #91
Reno, NV, USA, 27th November – 1st December 2017
Agenda item 6.2.6.1.1.2
R1-1721149

## Slide 2: Background
Working assumption for efeMTC in RAN1 #90bis
For idle mode,
  In specifying a power saving physical signal to indicate whether the UE needs to decode subsequent physical channel(s) for idle mode paging, select a candidate among the following power saving physical signals:
    ‘Wake-up signal or DTX’ with new periodic sync signal
    ‘Wake-up signal or DTX’ without new periodic sync signal
  Study till the next meeting how to ensure sufficient sync performance.
    Consider potential synergies with the WI objective on Reduced system acquisition time.
    Consider impacts from mobility.

## Slide 3: Proposal
UE should be assumed to synchronized to the network before detecting the WUS
WUS configuration is signaled by SI
The WUS location in relation to its associated PO is the same for eDRX and DRX
  That is, for eDRX, the location of the WUS is set in relation to the first PO immediately following the WUS
The maximum WUS length in a cell is configurable
Each WUS is transmitted aligned to the end of the WUS
  Or FFS between beginning and end
Further study the benefits of TX diversity in WUS design