## Slide 1: WF on search space for explicit HARQ-ACK feedback
ZTE , Sanechips, …
3GPP TSG RAN WG1 Meeting #91
Reno, USA, November 27th – December 1st, 2017
Agenda item 6.2.5.4
R1-1721159

## Slide 2
Background
  Interval of existing SS is semi-static configured by RRC, which may be not matched with dynamic PUSCH scheduling with different repetitions. For example, SS internal is 320 subframes and the number of PUSCH repetitions is 256. In this case, early PUSCH termination cannot be applied because there is no search space available for transmitting HARQ-ACK feedback during PUSCH transmission period.

## Slide 3
Observation
  For reception of HARQ-ACK feedback for early termination of PUSCH transmission, semi-static configuration of SS interval may be not matched with dynamic PUSCH scheduling with different repetitions.

## Slide 4
Proposal
  During PUSCH transmission period, new search space for reception of explicit HARQ-ACK feedback for early PUSCH termination can be supported.
    FFS: location of new search space
    FFS: how to enable/trigger monitoring of new search space.