## Slide 1: WF on DL Channel Power Saving Signal in efeMTC
Ericsson, Nokia, NSB, Sony, Sierra Wireless, …
3GPP TSG RAN WG1 Meeting #91 R1-1721164
Reno, NV, USA, 27th November – 1st December 2017
Agenda item 6.2.5.3

## Slide 2: Background
Working assumption for efeMTC in RAN1 #90bis
For idle mode,
  In specifying a power saving physical signal to indicate whether the UE needs to decode subsequent physical channel(s) for idle mode paging, select a candidate among the following power saving physical signals:
    ‘Wake-up signal or DTX’ with new periodic sync signal
    ‘Wake-up signal or DTX’ without new periodic sync signal
  Study till the next meeting how to ensure sufficient sync performance.
    Consider potential synergies with the WI objective on Reduced system acquisition time.
    Consider impacts from mobility.

## Slide 3: Proposal
The WUS does not explicitly provide synchronization
‘WUS or DTX’ with new periodic sync is selected as power saving signal
The WUS configuration is signaled by SI
The time location of the WUS is set in relation to the following PO
The [maximum] WUS length in a cell is configurable
Further study the benefits of diversity methods (TX, FH) in WUS design