## Slide 1: WF on capabilities and configuration of UL HARQ-ACK feedback for MTC
Ericsson, Intel, Qualcomm
3GPP TSG-RAN WG1 Meeting #91
Reno, Nevada, USA, 27th November – 1st December 2017
Agenda item 6.2.5.4
R1-1721171

## Slide 2: Background
RAN1#90bis agreements:
  Early termination of PUSCH transmission is supported at least in FD-FDD and TDD by the following:
    MPDCCH for UL grant for scheduling new UL data
    MPDCCH for explicit HARQ-ACK feedback
  For explicit HARQ-ACK feedback for early termination of MPDCCH monitoring:
    Explicit HARQ-ACK feedback for a single UE is carried in a DCI with the same DCI size as DCI format 6-0A/B. The DCI is carried on MPDCCH in UE-specific search space.
  For explicit HARQ-ACK feedback for early termination of PUSCH transmission:
    Explicit HARQ-ACK feedback for a single UE is carried in a DCI with the same DCI size as DCI format 6-0A/B. The DCI is carried on MPDCCH in UE-specific search space.
    FFS: Explicit HARQ-ACK feedback for multiple UEs is carried in a DCI

## Slide 3: Proposals
From RAN1 point of view, the following can be bundled into a single optional UE capability for BL/CE UEs with UE capability signaling:
  Early termination of MPDCCH monitoring in RRC connected mode through explicit HARQ-ACK feedback
  Early termination of PUSCH transmission in RRC connected mode through explicit HARQ-ACK feedback
  Early termination of PUSCH transmission in RRC connected mode through UL grant for scheduling new UL data (i.e. “implicit HARQ-ACK feedback”)
The above functionality is enabled by eNB through RRC reconfiguration (1 bit)