## Slide 1: Way Forward on function of power saving signal for IDLE mode paging
Huawei, HiSilicon, ….
3GPP TSG RAN WG1 Meeting #91
RENO, USA, 27 November – 1 December 2017
Agenda item 6.2.6.1.1.1
R1-1721180

## Slide 2: Background
In RAN1#90bis, it was agreed:
  Working assumption: WUS/DTX is adopted for the power saving signal for IDLE mode paging;
  The UE is configured with a transmission duration of WUS by higher layers
  The WUS signal may be decoded with or without relying on prior synchronization
    Whether the UE needs to acquire (further) synchronization using NPSS/NSSS to decode the NPDCCH following the WUS is FFS
    The power saving of using existing synchronization signal to achieve sync and using WUS for synchronization should be compared.
    For RAN#78 timeline, RAN4 can assume the UE is synchronized prior to the WUS
    After RAN#78, RAN1 and RAN4 will conduct additional work to allow the assumption that the UE is not synchronized prior to the WUS (with the same WUS signal design) for 144 dB MCL; and will study to allow the assumption that the UE is not synchronized prior to the WUS (with the same WUS signal design) for 154, 164 dB MCL
      Status of work on ‘Relaxed monitoring for cell reselection’ in RAN2/4 should be considered

## Slide 3
Proposals:
Confirm the WA: WUS/DTX is adopted for the power saving signal for IDLE mode paging.
To resolve FFS on the WUS with synchronization function, further discuss:
    Opt1: UE needs to acquire synchronization using NPSS/NSSS to decode the NPDCCH following the WUS
    Opt2: UE uses WUS to acquire synchronization using WUS to decode the NPDCCH following the WUS for DRX case and DRX within PTW of eDRX case;
    Opt3: UE uses WUS to acquire synchronization using WUS to decode the NPDCCH following the WUS at least for DRX case and eDRX case with short eDRX cycle;
Request RAN2 to consider the implication on RRM measurement by using NPSS/NSSS and possible relaxations