## Slide 1: Way Forward on NRS in TDD NB-IoT
Huawei, HiSilicon, ZTE, SaneChips
3GPP TSG RAN WG1 Meeting #91
Reno, USA, November 27 - December 1, 2017
Agenda item 6.2.6.3.1
R1-1721212

## Slide 2: Background
In FDD NB-IoT, NRS is mapped to symbol #5 and symbol #6 of 2 slots in a subframe shown in Fig. 1
Fig.1 NRS mapping in FDD
In TDD NB-IoT, NRS should be determined.

## Slide 3: Proposal
For NRS transmission in TDD NB-IoT:
  In downlink subframes, NRS is mapped in symbol 5 and 6 of 2 slots, i.e. the same as FDD
  In special subframe:
    For special subframe configurations 1, 2, 6, 7, NRS mapping is downselect among the following two options.
      Option 1: NRS is mapped in symbol 5 and 6 of the first slot, i.e. the same as FDD
      Option 2: NRS is mapped in symbol 2, 3, 5 and 6 of the first slot
    For special subframe configurations 9, 10, NRS is mapped in symbol 2, 3 of the first slot.
    For special subframe configurations 3, NRS is mapped in symbol 2, 3 of 2 slots.
    For special subframe configurations 4 and 8 if supported, NRS is mapped in symbol 2, 3 of 2 slots
    FFS the special subframe configurations 0 and 5