## Slide 1: Way Forward on HARQ in TDD NB-IoT
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #91
Reno, USA, November 27 - December 1, 2017
Agenda item 6.2.6.3.3
R1-1721214

## Slide 2: Background
In FDD NB-IoT, two HARQ process is an optional UE capability.
In TDD NB-IoT, HARQ may need some changes due to discontinuous downlink and uplink subframes.

## Slide 3: Proposal
Supporting two HARQ processes is an optional UE capability in NB-IoT TDD system.
  The minimum gap between transmissions corresponding to one DL or UL HARQ process is the same as FDD.
    FFS details of scheduling delays, etc.
  A UE supporting and configured to use 2 HARQ processes can be scheduled to transmit in UL subframes that occur during a DL reception, and receive in DL subframes that occur during a UL transmission.
    FFS the combinations of DL and UL transmissions that can be scheduled in this way
    FFS any changes on timing relationships between the two HARQ processes