## Slide 1: On UL power sharing for coverage enhancement
Orange, NTT Docomo, AT&T, China Telecom, China Unicom, DT, Verizon, Bouygues Telecom, Huawei, ZTE, Ericsson, CATT, OPPO, Vivo, Xiaomi, Apple, Hisilicon
R1-1721502
3GPP TSG RAN WG1 AI 7.6.1

## Slide 2: Backgrounds (1/3)
Agreement RAN1#90 on UL power control
  At least for LTE-NR NSA operation
    Maximum allowed power values for LTE (P_LTE) and NR (P_NR) are set separately
      i.e., when UE is configured for NR, P_LTE can be configured up to P_cmax and P_NR can be configured up to P_cmax.
      e.g. P_LTE + P_NR > P_cmax or P_LTE + P_NR = P_cmax
    Signaling details for P_LTE, P_NR are left to RAN2, RAN4.
    Note: ‘P_cmax’ is a limit that is similar to ‘The configured maximum UE output power’ that was specified for LTE.
    Note: The network will still have flexibility to prioritize or reserve certain NR transmission power depending on network implementation
    All UEs are mandated to handle P_LTE + P_NR = P_cmax while handling of P_LTE + P_NR > P_cmax depends on UE capability
    At least, when DL/UL LTE sTTI/reduced UE processing time based operation is not configured for the UE, if total transmit power exceeds P_cmax when there is simultaneous NR and LTE UL tx,
      For NR, UE scales down/drops NR transmission and NR power scaling details are left to UE implementation (note: it is not intended to have RAN4 test from RAN1 perspective)
        If there are two or more UL carriers, the power scaling or tx dropping can be performed for each of the UL carriers separately or jointly up to UE implementation
      For LTE, no change in power control procedure
    FFS the case when DL/UL LTE sTTI/reduced UE processing time based operation is configured for the UE
    The following is FFS
      The case when P_NR is configured such that P_NR < P_cmax, and UE can use power up to P_cmax in NR when it knows that there will be no UL transmission in LTE by semi-static configuration (e.g., measurement gap, DL/UL configuration)

## Slide 3: Background (2/3)
Time resource allocation is not equivalent to power allocation for coverage improvement
  Under a delay constraint increasing the transmission power is the only solution

## Slide 4: Background (3/3)
Agreement NR AH#2 on scenarios for UL coverage improvement
  RAN1 should consider the following scenarios as listed in R1-1711817 in the future work especially in terms of UL coverage
    Scenario 1
    Scenario 2 where UL sharing is from network perspective
      FFS where UL sharing from UE perspective
        Aim to conclude in the next meeting; if no consensus, consider sending an LS to RANP for clarification
    Scenario 3
Agreement RAN1#90
  Define the necessary mechanisms to ensure that NR-PUSCH which carries only control information can reach a similar coverage as NR DL control in scenario 1
Full power transmission for NR or LTE when the UE is configured in TDM/single Tx from the network perspective is beneficial for the coverage of all scenarios

## Slide 5: Proposals
For LTE/NR NSA operation,
  All UEs capable of LTE/NR NSA operation shall support single UL operation with case 1 mechanism (SUO-C1) and can be semi-statically configured by the network in SUO-C1.
  UEs configured in SUO-C1are mandated to handle P_LTE = P_cmax and P_NR = P_cmax. Note :
      Scheduler ensures that no simultaneous transmissions occur for a given UE.
      In case simultaneous transmissions are scheduled, UE behavior is not specified.