## Slide 1
3GPP TSG RAN WG1 #91 R1-1721670
Reno, USA, November 27th – December 1st, 2017
Agenda item: 7.2.2.4
WF for BFR Candidate Beam Selection
Huawei, HiSilicon, Mediatek, LGE, Intel, NEC, Lenovo, Motorola Mobility, Spreadtrum, ATT, Fujitsu, Ericsson, [interdigital], [Samsung], [NTT Docomo]

## Slide 2: Background and Proposal
Background
  With BLER as the BFD metric, L1-RSRP as the NBI metric, the old beam that triggers the BLER failure may very well be selected as a new identified beam because it satisfies the L1-RSRP metric.
  Potential Issues
    Unnecessary false alarm for serving cell
    Unnecessary interference for adjacent cells
    Unnecessary power draining for user equipment
Proposal: If one or more candidate beams other than a previous serving beam satisfy new beam identification threshold, a UE shall not choose the previous serving beam as a new identified beam for beam failure recovery, before the Beam-Failure-Recovery-Timer expires.