## Slide 1
WF on Aperiodic TRS
Qualcomm, Ericsson, …
3GPP TSG RAN WG1 #91
Reno, NV, USA, Nov 27 – Dec 1 2017
Agenda: 7.2.3.6
R1-1721701

## Slide 2: Backgrounds
Aperiodic TRS is essential given we have many aperiodic events as well as some periodic events which may not be aligned with periodic TRS.
  SCell activation
    Without aperiodic TRS, SCell activation can be delayed further up to TRS periodicity (max 80 ms on top of activation delay), not acceptable.
  mmW beam change
    Without aperiodic TRS, data reception can be delayed up to TRS periodicity (max 80 ms), not acceptable.
      It is assumed that UE is not tracking TRS from multiple beams simultaneously
  Connected mode DRX
    Without aperiodic TRS, it requires UE to wake up in the middle of CDRX off when periodic TRS is not aligned with CDRX on-duration, not desirable for CDRX feature.
  Idle mode DRX
    Without aperiodic TRS, it requires UE to wake up before paging occasion when SSB is not aligned with paging occasion, affecting standby time reduction roughly to 1/2,not acceptable.

## Slide 3: Proposals
Aperiodic TRS is supported in NR at least for following use cases
  SCell activation
    Aperiodic TRS can be triggered via DCI after SCell activation
  Beam changes
    Aperiodic TRS can be triggered via DCI after PDCCH/PDSCH beam changes.
  Connected mode DRX
    Alt 1
      Support aperiodic TRS before CDRX on-duration. The offset between aperiodic TRS and CDRX on-duration can be UE specifically configured.
      UE assumes aperiodic TRS is transmitted before CDRX on-duration when UE is expected to be scheduled.
    Alt 2
      Support aperiodic TRS during CDRX on-duration via DCI-triggered aperiodic TRS
      Note: UE performance on PDCCH monitoring is not guaranteed until aperiodic TRS is received.
    UE assumes periodic TRS may not be transmitted during CDRX off state.
  Idle mode DRX
    Support aperiodic TRS before IDRX paging occasion
      FFS: details on configuration signaling
    UE assumes aperiodic TRS is transmitted before Idle paging occasion when UE is expected to be paged.