## Slide 1: Proposals for 7.3.3.4
NTT DOCOMO
R1-1721705
3GPP TSG RAN WG1#91
Reno, USA, Nov. 27 – Dec. 1, 2017
Agenda item 7.3.3.4

## Slide 2: Proposal 1
Activation and deactivation signaling for Type 2 UL transmission without UL grant/DL SPS is differentiated by different values of two fields in the DCI.
  FFS details.

## Slide 3: Proposal 1
For Type 2 UL transmission without UL grant/DL SPS,
  Two fields are used to identify whether the DCI activates or de-activates the UL grant/DL SPS.
    FFS details.

## Slide 4: Proposal 2
For UL transmission without UL grant, the initial transmission of the K repetitions of a TB can start at any transmission occasion within the period P, and repetitions end at the last transmission occasion within the period P
  At least RV sequence is mapped on to the transmission occasions within the period P
Supported by: DCM, Huawei, HiSilicon, MTK, Vivo, Interdigital, NICT, TCL, LGE, Sharp, Convida Wireless, CATT, CATR, ITRI, CMCC, Orange, Xiaomi, China Unicom, Sequans, China Telecom, Sony, Fraunhofer IIS, Hughes, Vodafone, [ZTE], [OPPO]
P
…
Packet arrival
Real transmission

## Slide 5: Proposal 3
For UL transmission without UL grant, the HARQ ID associated with the K repetitions of a TB is derived from the following equation:
  HARQ Process ID = floor (X / UL-TWG-periodicity) mod UL-TWG-numbHARQproc
    Where e.g., X= (SFN * SlotPerFrame * SymbolPerSlot + Slot_index_In_SF * SymbolPerSlot + Symbol_Index_In_Slot)
    X refers to the first transmission occasion of repetition bundle takes place.

## Slide 6: LTE HARQ ID determination
HARQ Process ID = [floor(CURRENT_TTI/semiPersistSchedIntervalDL)] modulo numberOfConfSPS-Processes,
  where CURRENT_TTI=[(SFN * 10) + subframe number].
  CURRENT_TTI refers to the TTI where first transmission of repetition bundle takes place.