## Slide 1: WF on Accumulative Closed-Loop TPC Command Qualcomm, …
3GPP TSG RAN WG1 91 R1-1721706
Reno, USA
27th Nov. – 1st December, 2017
Agenda item: 7.6.1
Document for decision

## Slide 2: Background
Agreements (RAN1 90 bis):
  For closed loop power control process, f(i) in case of accumulative TPC command mode can be reset by RRC reconfiguration of P_0 and alpha
Exactly when and how f(i), in case of accumulative TPC command mode, is reset or inherited is not clearly defined

## Slide 3: Discussion
The accumulative closed-loop TPC command carries useful information and should be carried over unless open-loop power control parameter P_0 or alpha changes.
However, in case of a large changed of pathloss due to beam switch, excessive power may be transmitted by UE if f(i) is carried over without any change.
  The receive signal power levels using source and destination beams are respectively:
    Where PLS,L3 is the L3 path loss and PLS,L1 is the path loss calculated based on latest RSRP of source beam; PLd,L3 is the L3 path loss and PLd,L1 is the path loss calculated based on latest RSRP of destination beam.
  The excessive power transmitted is:

## Slide 4: Proposals
For the closed-loop TPC commands, f(i), g(i), in accumulative mode in case of reconfiguration of RS resource(s) index, k,
  if open-loop parameters, P_0 and/or alpha, are reconfigured, f(i)/g(i) is reset to be 0 in case of reconfiguration of open-loop parameters, P_0 and/or alpha.
  If open-loop parameters, P_0 and alpha, are not reconfigured, fd(i)= fs(i)-Delta for PUSCH and gd(i)= gs(i) -Delta for PUCCH with Delta being any value in the range [0, ].
    PLS,L3 is the L3 path loss of source beam and PLS,L1 is the path loss calculated based on latest RSRP of the source beam; PLd,L3 is the L3 path loss and PLd,L1 is the path loss calculated based on latest RSRP of the destination beam.
    Exact value within the range is up to UE implementation.