## Slide 1: Proposal for 7.3.3.4
NTT DOCOMO
R1-1721718
3GPP TSG RAN WG1#91
Reno, USA, Nov. 27 – Dec. 1, 2017
Agenda item 7.3.3.4

## Slide 2: Proposal
For UL transmission without UL grant, the initial transmission of the K repetitions of a TB can start at any configured transmission occasion within a period P, and repetitions end at the last transmission occasion within the period P, when the UE is configured with RV sequence of {0,0,0,0}.
When the UE is configured with RV sequence of {0,2,3,1}, the initial transmission of the K repetitions of a TB shall start at the first transmission occasion within a period
  FFS RV sequence of {0,3,0,3}
The RV used for initial transmission is determined based on the following:
  nth transmission occasion within the period is the MOD (n, 4)-th RV in the sequence
P
…
Packet arrival
Real transmission

## Slide 3: Back up

## Slide 4: Proposal version 1
For UL transmission without UL grant, the initial transmission of the K repetitions of a TB can start at any transmission occasion within a period P, and repetitions end at the last transmission occasion within the period P, except when the UE is configured with RV sequence of {0,2,3,1}.
RV sequence starts from the first transmission occasion of a repetition bundle, and UE determines the RV value for each repetition based on the transmission occasion where the repetition occurs.
P
…
Packet arrival
Real transmission

## Slide 5: Proposal version 2
For UL transmission without UL grant, the initial transmission of the K repetitions of a TB can start at any transmission occasion within a period P, and repetitions end at the last transmission occasion within the period P, except when the UE is configured with RV sequence of {0,2,3,1}.
The RV used for initial transmission follows the RV that would be applied to that transmission occasion assuming the transmission started in the first transmission occasion within the period.
P
…
Packet arrival
Real transmission