## Slide 1
3GPP TSG RAN WG1#91 R1-17XXXXX
Reno, USA, November 27th – December 1st, 2017
Agenda item: 7.1.2.2
Summary of Offline Discussion on RMSI CORESET Configuration
Samsung

## Slide 2: Proposal 1
The frequency offset in PRB level between RMSI CORESET and SS/PBCH block in the table is define as the frequency difference from the lowest PRB of RMSI to the lowest PRB of SS/PBCH block
  Note: The offset in subcarrier level between the edge of SS/PBCH block PRB and RMSI CORESET PRB grid is indicated by PRB grid offset (SSB-subcarrier-offset) in PBCH (5 bits for below-6GHz and 4 bits for above-6GHz)
For each of the following combination of SS/PBCH SCS and RMSI CORESET SCS, the multiplexing patterns between SS/PBCH block and RMSI (CORESET and PDSCH), RMSI CORESET BW, RMSI CORESET duration, and PRB-level offset are jointly coded in a table using 4 bits of RMSI configuration in NR-PBCH.
  {SSB SCS, RMSI SCS} = {15, 15}, {15, 30}, {30, 15}, {30, 30}, {120, 60}, {120,120},{240, 60}, {240, 120}} kHz

## Slide 3: Proposal 2
Definition for the multiplexing pattern tables SS/PBCH SCS and RMSI CORESET SCS
  “Pattern 1” refers to the multiplexing pattern that SS/PBCH block and RMSI CORESET occur in different time instances, and SS/PBCH block TX BW and the initial active DL BWP containing RMSI CORESET overlap
  “Pattern 2” refers to the multiplexing pattern that SS/PBCH block and RMSI CORESET occur in different time instances, and SS/PBCH block TX BW and the initial active DL BWP containing RMSI CORESET do not overlap
  “Pattern 3” refers to the multiplexing pattern that SS/PBCH block and RMSI CORESET occur in the same time instance, and SS/PBCH block TX BW and the initial active DL BWP containing RMSI CORESET do not overlap
  Note: The following figure is for information purpose only.

## Slide 4: Proposal 3
For the combination of SS SCS = 15 kHz and RMSI CORESET SCS = 15 kHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 24 | 2 | 0
2 | Pattern 1 | 24 | 2 | 2
3 | Pattern 1 | 24 | 2 | 4
4 | Pattern 1 | 24 | 3 | 0
5 | Pattern 1 | 24 | 3 | 2
6 | Pattern 1 | 24 | 3 | 4
7 | Pattern 1 | 48 | 1 | 12
8 | Pattern 1 | 48 | 1 | 16
9 | Pattern 1 | 48 | 2 | 12
10 | Pattern 1 | 48 | 2 | 16
11 | Pattern 1 | 48 | 3 | 12
12 | Pattern 1 | 48 | 3 | 16
13 | Pattern 1 | 96 | 1 | 38
14 | Pattern 1 | 96 | 2 | 38
15 | Pattern 1 | 96 | 3 | 38
16 | Reserved |  |  | 

## Slide 5: Proposal 4
For the combination of SS SCS = 15 kHz and RMSI CORESET SCS = 30 kHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 24 | 2 | 6
2 | Pattern 1 | 24 | 2 | 7
3 | Pattern 1 | 24 | 2 | 8
4 | Pattern 1 | 24 | 3 | 6
5 | Pattern 1 | 24 | 3 | 7
6 | Pattern 1 | 24 | 3 | 8
7 | Pattern 1 | 48 | 1 | 18
8 | Pattern 1 | 48 | 1 | 20
9 | Pattern 1 | 48 | 2 | 18
10 | Pattern 1 | 48 | 2 | 20
11 | Pattern 1 | 48 | 3 | 18
12 | Pattern 1 | 48 | 3 | 20
13 | Reserved |  |  | 
14 | Reserved |  |  | 
15 | Reserved |  |  | 
16 | Reserved |  |  | 

## Slide 6: Proposal 5
For the combination of SS SCS = 30 kHz and RMSI CORESET SCS = 15 kHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 48 | 1 | 2
2 | Pattern 1 | 48 | 1 | 6
3 | Pattern 1 | 48 | 2 | 2
4 | Pattern 1 | 48 | 2 | 6
5 | Pattern 1 | 48 | 3 | 2
6 | Pattern 1 | 48 | 3 | 6
7 | Pattern 1 | 96 | 1 | 28
8 | Pattern 1 | 96 | 2 | 28
9 | Pattern 1 | 96 | 3 | 28
10 | Reserved |  |  | 
11 | Reserved |  |  | 
12 | Reserved |  |  | 
13 | Reserved |  |  | 
14 | Reserved |  |  | 
15 | Reserved |  |  | 
16 | Reserved |  |  | 

## Slide 7: Proposal 6
For the combination of SS SCS = 30 kHz and RMSI CORESET SCS = 30 kHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 24 | 2 | 0
2 | Pattern 1 | 24 | 2 | 1
3 | Pattern 1 | 24 | 2 | 2
4 | Pattern 1 | 24 | 2 | 3
5 | Pattern 1 | 24 | 2 | 4
6 | Pattern 1 | 24 | 3 | 0
7 | Pattern 1 | 24 | 3 | 1
8 | Pattern 1 | 24 | 3 | 2
9 | Pattern 1 | 24 | 3 | 3
10 | Pattern 1 | 24 | 3 | 4
11 | Pattern 1 | 48 | 1 | 12
12 | Pattern 1 | 48 | 1 | 14
13 | Pattern 1 | 48 | 1 | 16
14 | Pattern 1 | 48 | 2 | 12
15 | Pattern 1 | 48 | 2 | 14
16 | Pattern 1 | 48 | 2 | 16

## Slide 8: Proposal 7
For the combination of SS SCS = 120 kHz and RMSI CORESET SCS = 60 kHz
  Note: configurations 13, 14, 15, and 16 supported only when BW > 100MHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 48 | 1 | 0
2 | Pattern 1 | 48 | 1 | 8
3 | Pattern 1 | 48 | 2 | 0
4 | Pattern 1 | 48 | 2 | 8
5 | Pattern 1 | 48 | 3 | 0
6 | Pattern 1 | 48 | 3 | 8
7 | Pattern 1 | 96 | 1 | 28
8 | Pattern 1 | 96 | 2 | 28
9 | Pattern 2 | 48 | 1 | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
10 | Pattern 2 | 48 | 1 | [49]
11 | Pattern 2 | 48 | [2] | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
12 | Pattern 2 | 48 | [2] | [49]
13 | Pattern 2 | [96] | 1 | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
14 | Pattern 2 | [96] | 1 | [97]
15 | Pattern 2 | [96] | [2] | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
16 | Pattern 2 | [96] | [2] | [97]

## Slide 9: Proposal 8
For the combination of SS SCS = 120 kHz and RMSI CORESET SCS = 120 kHz
  Note: configurations 7and 8 supported only when BW > 100MHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 24 | 2 | 0
2 | Pattern 1 | 24 | 2 | 4
3 | Pattern 1 | 48 | 1 | 14
4 | Pattern 1 | 48 | 2 | 14
5 | Pattern 3 | 24 | 2 | [-21] if PRG grid not aligned and [-20] if PRG grid aligned
6 | Pattern 3 | 24 | 2 | 24
7 | Pattern 3 | [48] | 2 | [-21] if PRG grid not aligned and [-20] if PRG grid aligned
8 | Pattern 3 | [48] | 2 | [48]
9 | Reserved |  |  | 
10 | Reserved |  |  | 
11 | Reserved |  |  | 
12 | Reserved |  |  | 
13 | Reserved |  |  | 
14 | Reserved |  |  | 
15 | Reserved |  |  | 
16 | Reserved |  |  | 

## Slide 10: Proposal 9
For the combination of SS SCS = 240 kHz and RMSI CORESET SCS = 60 kHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 96 | 1 | 0
2 | Pattern 1 | 96 | 1 | 16
3 | Pattern 1 | 96 | 2 | 0
4 | Pattern 1 | 96 | 2 | 16
5 | Reserved |  |  | 
6 | Reserved |  |  | 
7 | Reserved |  |  | 
8 | Reserved |  |  | 
9 | Reserved |  |  | 
10 | Reserved |  |  | 
11 | Reserved |  |  | 
12 | Reserved |  |  | 
13 | Reserved |  |  | 
14 | Reserved |  |  | 
15 | Reserved |  |  | 
16 | Reserved |  |  | 

## Slide 11: Proposal 10
For the combination of SS SCS = 240 kHz and RMSI CORESET SCS = 120 kHz
  Note: configurations 9, 10, 11, 12 supported only when BW > 100MHz
Configuration Index | Multiplexing Pattern | CORESET BW in PRB | Number of Symbols for CORESET | Frequency Offset in PRB of RMSI CORESET numerology
1 | Pattern 1 | 48 | 1 | 0
2 | Pattern 1 | 48 | 1 | 8
3 | Pattern 1 | 48 | 2 | 0
4 | Pattern 1 | 48 | 2 | 8
5 | Pattern 2 | 24 | 1 | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
6 | Pattern 2 | 24 | 1 | [25]
7 | Pattern 2 | 24 | [2] | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
8 | Pattern 2 | 24 | [2] | [25]
9 | Pattern 2 | [48] | 1 | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
10 | Pattern 2 | [48] | 1 | [49]
11 | Pattern 2 | [48] | [2] | [-42] if PRG grid not aligned and [-41] if PRG grid aligned
12 | Pattern 2 | [48] | [2] | [49]
13 | Reserved |  |  | 
14 | Reserved |  |  | 
15 | Reserved |  |  | 
16 | Reserved |  |  | 

## Slide 12: Appendix

## Slide 13: Summary for Multiplexing Pattern 1
SS SCS (kHz) | CORESET SCS (kHz) | CORESET BW (PRB in CORESET numerology) | Min # configurations of frequency offset | Center frequency offset value in PRB of CORESET numerology | Edge frequency offset value in PRB of CORESET numerology
15 | 15 | 24 | 3 | -2a, 0, 2a | 0, 2, 4
15 | 15 | 48 | 2 | -2a, 2a | 12, 16
15 | 15 | 96 | 1 | 0 | 38
15 | 30 | 24 | 3 | -2a, 0, 2a | 6, 7, 8
15 | 30 | 48 | 2 | -2a, 2a | 18, 20
30 | 15 | 48 | 2 | -a, a | 2, 6
30 | 15 | 96 | 1 | 0 | 28
30 | 30 | 24 | 5 | -2a, -a, 0, a, 2a | 0, 1, 2, 3, 4
30 | 30 | 48 | 3 | -2a, 0, 2a | 12, 14, 16
120 | 60 | 48 | 2 | -2a, 2a | 0, 8
120 | 60 | 96 | 1 | 0 | 28
120 | 120 | 24 | 2 | -2a, 2a | 0, 4
120 | 120 | 48 | 1 | 0 | 14
240 | 60 | 96 | 2 | -2a, 2a | 0, 16
240 | 120 | 48 | 2 | -2a, 2a | 0, 8
  Note: a = SS SCS / CORESET SCS in the table

## Slide 14: Example 1
SS SCS = 15 kHz, CORESET SCS = 15 kHz, min CH BW = 5 MHz (25 PRBs for both SS and CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  3 configurations are sufficient to indicate the frequency offset: 0, 2, 4

## Slide 15: Example 2
SS SCS = 15 kHz, CORESET SCS = 15 kHz, TX BW = 10 MHz (52 PRBs for both SS and CORESET), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  Note that the configurations TX BW = 10 MHz will be reused for TX BW = 20 MHz
  2 configurations are sufficient to indicate the frequency offset: 12, 16

## Slide 16: Example 3
SS SCS = 15 kHz, CORESET SCS = 15 kHz, TX BW = 20 MHz (106 PRBs for both SS and CORESET), RMSI CORESET BW = 96 PRBs (in RMSI numerology)
  1 configuration is sufficient to indicate the frequency offset: 38

## Slide 17: Example 4
SS SCS = 15 kHz, CORESET SCS = 30 kHz, TX BW = 10 MHz (52 PRBs for SS and 24 PRBs for CORESET), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  Note that the configurations TX BW = 10 MHz will be reused for TX BW = 20 MHz
  3 configurations are sufficient to indicate the frequency offset: 6, 7, 8

## Slide 18: Example 5
SS SCS = 15 kHz, CORESET SCS = 30 kHz, TX BW = 20 MHz (106 PRBs for SS and [50] PRB for CORESET), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset: 18, 20

## Slide 19: Example 6
SS SCS = 30 kHz, CORESET SCS = 15 kHz, min CH BW = 10 MHz (24 PRBs for SS, and 52 PRBs for CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset: 2, 6

## Slide 20: Example 7
SS SCS = 30 kHz, CORESET SCS = 15 kHz, TX BW = 20 MHz ([50] PRBs for SS and 106 PRB for CORESET), RMSI CORESET BW = 96 PRBs (in RMSI numerology)
  1 configuration is sufficient to indicate the frequency offset: 28

## Slide 21: Example 8
SS SCS = 30 kHz, CORESET SCS = 30 kHz, min CH BW = 10 MHz (24 PRBs for both SS and CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  5 configurations are sufficient to indicate the frequency offset: 0, 1, 2, 3, 4

## Slide 22: Example 9
SS SCS = 30 kHz, CORESET SCS = 30 kHz, TX BW = 20 MHz ([50] PRB for both SS and CORESET), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  3 configurations are sufficient to indicate the frequency offset: 12, 14, 16

## Slide 23: Example 10
SS SCS = 120 kHz, CORESET SCS = 60 kHz, min CH BW = 50 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset : 0, 8

## Slide 24: Example 11
SS SCS = 120 kHz, CORESET SCS = 120 kHz, min CH BW = 50 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset: 0, 4

## Slide 25: Example 12
SS SCS = 240 kHz, CORESET SCS = 60 kHz, min CH BW = 100 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 96 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset: 0, 16

## Slide 26: Example 13
SS SCS = 240 kHz, CORESET SCS = 120 kHz, min CH BW = 100 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset: 0, 8