## Slide 1: Multiplexing rules for PUCCH resources with the same starting symbols
Ericsson
3GPP TSG RAN WG1 Meeting #92
Sanya, China, April 16th – 20nd, 2018
Agenda Item: 7.1.3.2.1
Source: Ericsson
Document for: Discussion and Decision
R1-1805698

## Slide 2: Background
Note: The following multiplexing rules are specified for overlapped AN and SR PUCCH resources with the same starting symbols.
 | AN PF0 | AN PF1 | AN PF2/3/4
SR PF0 | specified | Not. Spec. | specified
SR PF1 | specified | specified | specified
CSI PF2/3/4 | specified | specified | specified

## Slide 3: Background
Agreement (RAN1#91):
When AN/SR and CSI PUCCH resources have the same starting symbols, one PUCCH resource is used for transmission of AN/SR and CSI.
    If the UE is configured with more than one PUCCH resource sets, the PUCCH resource set is determined based on the total number of AN/SR and CSI. The PUCCH resource is determined based on ARI.
      FFS on UE assumption on the CSI part 2 is present
      FFS if/how to multiplex CSI and AN/SR in case PUCCH format indicated by ARI for AN/SR and CSI is different from the configured PUCCH format for CSI.
    If the UE is configured with only one PUCCH resource set,
      FSS how to determine the PUCCH resource for transmission of UCI

## Slide 4: Background
Note: The following multiplexing rules are specified for overlapped AN/SR and CSI PUCCH resources with the same starting symbols.
 | AN/SR +CSI PUCCH resource PF2 | AN/SR +CSI PUCCH resource PF3/PF4
CSI1, CSI2 CSI is configured with F3/F4 | FFS1 | Covered in spec
CSI (only one part) CSI is configured with F2 | Covered in spec | FFS2

## Slide 5: Proposal 1
When HARQ-ACK PUCCH resource with F1 overlaps with SR PUCCH resource with F0 with the same starting symbol in a slot,
  Alt 1: The UE transmits only HARQ-ACK in the HARQ-ACK PUCCH resource ( i.e the UE does not transmit SR if it is positive).
    Intel, E//, QC, LG, Lenovo, CATT, Samsung, DCM, Nokia
  Alt 2: If SR is positive, the UE transmits SR and doesn’t transmit HARQ-ACK. Otherwise, the UE transmits HARQ-ACK in the HARQ-ACK PUCCH resource.
    Vivo, OPPO, ZTE

## Slide 6: Proposal 2
When AN/SR and configured CSI PUCCH resources based on PF3 or 4 have the same starting symbols in a slot, when the UE determines the PUCCH resource set is based on the total number of AN/SR and CSI and the PUCCH resource based on ARI, if the PUCCH resource based on ARI for transmitting HARQ-ACK/SR and CSI is determined to PF2, select from one of the following alternatives:
  Alt. 1: This is an error case. UE is not expected to transmit AN/SR and CSI using the PUCCH format 2.
    Supportive companies: MTK, Samsung, Intel, QC, E//, DCM
  Alt. 2: Drop CSI part 2 (if present). Transmit jointly encoded AN/SR and CSI part 1 on the determined PUCCH format 2 resource indicated by ARI using the mapping rules for PF2.
    Supportive companies: CATT, Nokia , OPPO, Lenovo, Vivo, MTK
  Alt.3: Transmit jointly encoded AN/SR and CSI part 1 and separately encoded CSI part 1 on the determined PUCCH format 2 resource indicated by ARI using the mapping rules for PF2.
    The total coded bits are formed by concatenation of jointly encoded AN/SR and CSI part 1 and separately encoded CSI part 2 for mapping on PUCCH resources.
    Supportive companies: LG

## Slide 7: Proposal 3
When AN/SR and CSI PUCCH resources have the same starting symbols in a slot, for a wideband semi-persistent/periodic CSI reporting based on a PUCCH format 2, if the PUCCH resource based on ARI for transmitting HARQ-ACK/SR and CSI is based on format 3:
  CSI (only CSI part 1) is jointly encoded with HARQ-ACK/SR, following the existing procedure of encoding and mapping on resources for PUCCH format 3 or 4 to transmit the UCI.
    Supportive companies: E//, Nokia, MTK , Intel, LG, OPPO, Vivo, HW, DCM

## Slide 8: Proposal 4
When AN/SR and CSI PUCCH resources have the same starting symbols in a slot, if the UE is configured with only one PUCCH resource set, select from one of the following alternatives:
  Alt 1: This is a mis-configuration. The UE is not expected to transmit the corresponding HARQ-ACK/SR and the CSI report in a PUCCH resource in that slot.
    Supportive companies: E//, Intel, OPPO, QC, HW, Samsung, DCM
  Alt 2: HARQ-ACK/SR and CSI are transmitted together by PUCCH resource for CSI
    Supportive companies: Nokia, MTK, Lenovo, Motorola, CATT, ZTE
  Alt 3: HARQ-ACK/SR is transmitted on the HARQ-ACK/SR PUCCH resource and CSI reporting is dropped in that slot.
    Supportive companies: LG, Vivo

## Slide 9: Appendix

## Slide 10: Background
The multiplexing of overlapping SR and AN PUCCH resources with the same starting points is agreed.
However, when the starting points of PUCCH resources are different, solutions are summarized as below [R1-1805560].
  Alt 1: Multiplex total UCI on one PUCCH resource (Conditioned to ensure enough processing time).
    Nokia, MTK, LG, HW, Samsung, Ericsson
  Alt 2: Multiplex total UCI on one PUCCH resource if AN starts earlier than SR. Otherwise transmit the earliest transmission (due to UE implantations and processing time).
    Intel, QC, Ericsson, Panasonic
  Alt 3: One or more PUCCH transmissions based on Mux, dropping or puncturing methods (due to low latency applications)
    OPPO, Vivo, CATT, ZTE, Lenovo, Motorola, III
During the offline discussion, we discussed how to compromise Alt 1 and Alt 2 solutions in case of AN PUCCH resource overlapping with SR or CSI PUCCH resource.

## Slide 11: Illustrations (offline compromised Alt 1 and Alt2)
SR or P_CSI
AN
PDSCH
T1=N1+y
SR or P_CSI
AN
PDSCH
DCI
T1=N1+y
SR or P_CSI
AN
PDSCH
DCI
T1=N1+y
T2=N2+x
T2=N2+x
x,y are non-negative. FFS: x,y
T2=N2+x
DCI

## Slide 12: Proposal (offline compromised Alt 1 and Alt2 – Tuesday night)
When AN PUCCH resource partially overlap with an SR PUCCH resource or a CSI PUCCH resource, respectively, in a slot,
  If the first symbol of the earlier PUCCH, starts no earlier than symbol T1 and no earlier than T2, the UE transmits HARQ-ACK and SR or CSI respectively, using the same UCI multiplexing rule for the HARQ-ACK and SR or CSI, respectively, with same starting symbols.
  Otherwise, it is considered as an error case.
  T1=N1+x and T2=N2+y where x and y are non-negative integer values.
  FFS on values of x and y
  FFS multiplexing rule when AN PUCCH resource with F1 overlaps with SR PUCCH resource with F0.
  Note: The following multiplexing rules are specified for overlapped AN and SR PUCCH resources with the same starting symbols.
 | AN PF0 | AN PF1 | AN PF2/3/4
SR PF0 | specified | Not. Spec. | specified
SR PF1 | specified | specified | specified
CSI PF2/3/4 | specified | specified | specified

## Slide 13: Proposal
When CSI PUCCH resource partially overlap with an SR PUCCH resource, in a slot,
  the UE transmits CSI and SR using the same UCI multiplexing rule for the CSI and SR, with same starting symbols.
  Note: The following multiplexing rules are specified for overlapped AN and SR PUCCH resources with the same starting symbols.
 | SR PF0 | SR PF1
CSI PF2/3/4 | specified | specified