## Slide 1: Issue on EN-DC Dynamic Power Sharing with LTE SPS UL Skipping
Motorola Mobility, Lenovo
3GPP TSG RAN WG1 Meeting #94
Gothenburg, Sweden, Aug 20-24, 2018
Agenda 7.1.4
R1-1809874

## Slide 2: Discussion
LTE-SPS periodicity can be as short as 1ms to support low latency
LTE can be configured with UL skipping to skip UL transmission on PUSCH when there is no UL data in the transmit buffer
When LTE decides to skip UL transmission is implementation dependent and can be as late as 0.5ms from the start of the UL transmission
  To enable low latency applications with short SPS periodicity configuration
Current EN-DC power control procedure with dynamic power sharing (Type 1 UE), assumes NR has knowledge of LTE transmission with 3ms LTE timeline
Need to allow for NR relaxation (at least for UE processing capability 1) for this case of tight LTE timeline for LTE-SPS with UL skipping configured to prevent MCG LTE degradation
  Avoid relaxation of MCG LTE-SPS timeline with UL skipping configured

## Slide 3: Proposal
Proposal is to allow NR to be conservative in power setting on LTE SPS subframes with UL skipping configured and actual LTE UL transmission is skipped
For dynamic power sharing in EN-DC, and the UE configured with skipUplinkTxSPS on MCG, UE may assume SPS uplink transmission are not skipped in SPS subframe i1 on MCG when determining the transmission power in time-overlapping UE transmission(s) in slot i2 of the SCG.