## Slide 1: 3GPP TSG RAN WG1 Meeting #94bis R1-1812059 Chengdu, China, October 8th – 12th, 2018 Agenda Item: 7.1.3.1 Source: Ericsson Document for: Information and Discussion
On DCI size matching

## Slide 2: Background
There are many DCI size budget check points in 38.212, in the field description, after field description and spread over DCI 0_0 and 1_0
It is important to have a common understanding how the size matching is performed exactly
  Otherwise, it may result in different understanding of DCI content
Companies are encouraged to investigate the issue
The issue should be resolved at RAN1#95

## Slide 3: Appendix
The slides below illustrate the issues

## Slide 4: Configuration 1: fallback in CSS + fallback in USS
DCI size budget is met
DCI 0_0 in CSS
(FD size determined by
initial UL BWP)
DCI 1_0 in CSS
(FD size determined by
CORESET#0/initial DL BWP)
Matched to
DCI 0_0 in USS
(FD size determined by
active UL BWP)
DCI 1_0 in USS
(FD size determined by
active DL BWP)
Matched to

## Slide 5: Configuration 2: fallback in CSS + non-fallback (in USS)
DCI size budget is met
  Corner case: 0_1 in USS and 1_1 in USS happen to be of the same size => 2 DCI sizes
  In general: 0_1 in USS and 1_1 in USS have different sizes => 3 DCI sizes
DCI 0_0 in CSS
(FD size determined by
initial UL BWP)
DCI 1_0 in CSS
(FD size determined by
CORESET#0/initial DL BWP)
DCI 0_1 in USS
DCI 1_1 in USS
Matched to

## Slide 6: Configuration 3 fallback in CSS + fallback in USS + non-fallback (in USS)
DCI 0_0 in CSS
(FD size determined by
initial UL BWP)
DCI 1_0 in CSS
(FD size determined by
CORESET#0/initial DL BWP)
DCI 0_1 in USS
DCI 1_1 in USS
Matched to
DCI 0_0 in USS
(FD size determined by
active UL BWP)
DCI 1_0 in USS
(FD size determined by
active DL BWP)
How to size match in this configuration?

## Slide 7: Configuration 3-A: fallback in CSS + fallback in USS + non-fallback (in USS)
DCI size budget is met in corner cases
  Trigger size match (if any) between 0_0 and 1_0 in USS
DCI 0_0 in CSS
(FD size determined by
initial UL BWP)
DCI 1_0 in CSS
(FD size determined by
CORESET#0/initial DL BWP)
DCI 0_1 in USS
DCI 1_1 in USS
Matched to
DCI 0_0 in USS
(FD size determined by
active UL BWP)
DCI 1_0 in USS
(FD size determined by
active DL BWP)
Matched to

## Slide 8: Configuration 3-B: fallback in CSS + fallback in USS + non-fallback (in USS)
DCI size budget is not met in general
  Corner case: 0_1 and 1_1 are the same
    If 0_0 and 1_0 happen to be the same => No problem (covered by the previous slide)
    Else, mechanism in the next slide is triggered
DCI 0_0 in CSS
(FD size determined by
initial UL BWP)
DCI 1_0 in CSS
(FD size determined by
CORESET#0/initial DL BWP)
DCI 0_1 in USS
DCI 1_1 in USS
Matched to
DCI 0_0 in USS
(FD size determined by
active UL BWP)
DCI 1_0 in USS
(FD size determined by
active DL BWP)

## Slide 9: Configuration 3-B: fallback in CSS + fallback in USS + non-fallback (in USS)
DCI size budget is not met => Trigger DCI 0_0/1_0 in USS to size match to the counterpart in CSS => DCI size budget met again
DCI 0_0 in CSS
(FD size determined by
initial UL BWP)
DCI 1_0 in CSS
(FD size determined by
CORESET#0/initial DL BWP)
DCI 0_1 in USS
DCI 1_1 in USS
Matched to
DCI 0_0 in USS
(FD size determined by
active UL BWP)
DCI 1_0 in USS
(FD size determined by
active DL BWP)
Matched to
Matched to
MISSING IN SPEC