## Slide 1
Highlights from RAN#85
RAN1 Chairman
3GPP TSG RAN WG1#98bis
Chongqing, China, October 14th – 20th, 2019
R1-1909941

## Slide 2: LTE
All RAN1 endorsed LTE CRs submitted to RAN#85 are approved
Minor updates on exiting Rel-16 LTE items:
  NB-IoT WID update as in RP-192313
    Specify support of UE specific DRX and consider expanding the current DRX range  No RAN1 impact
  LTE_terr_bcast WID update as in RP-191924
    Minor “editorial-like” update

## Slide 3: NR
All RAN1 endorsed NR CRs submitted to RAN#85 are approved
Study on IIIoT Channel Modelling was declared as complete with one note:
  Enhancements on how to capture dense multipath can be further discussed via email. If consensus is reached, a CR can be submitted to the maintenance agenda item. However, note that the newly introduced channel model can already be used even without the above enhancement
Rel-16 eURLLC/IIoT
  Down-scoping of IIOT and URLLC was endorsed in RP-192287
    Ethernet header compression: Add the impacted LTE specs for the WI, LTE work to start once NR principles are clear
    UE based enhancements for more resource efficient PDCP duplication by enhancing PDCP duplication activation/deactivation mechanism is lower priority until RAN#86
    Intra-UE prioritization & multiplexing: Continue work in RAN1 and RAN2, however with the limitation that RAN1 would not consider L1 multiplexing of different services in Release 16.
  The corresponding updated IIoT WID was approved in RP-192324

## Slide 4: NR – Cont’d
Rel-16 Power Savings (vs. MR-DC/CA)
  Clarification of RAN1 scope for combining dormancy and power saving signals was endorsed in RP-192326
    RANP tasks RAN2 to define dormancy behavior under MR-DC/CA WI
    In parallel, in the next quarter, RAN1, in consultation with RAN2, specifies L1 based mechanism for transitioning between ‘dormancy-like’ and ‘non-dormancy-like’ behavior on activated SCells under MC-DC/CA WI.
    Further study will be conducted if any additional UE behavior is needed when UE is also configured for receiving PDCCH based power saving signal/channel outside active time, and, if agreed, the additional UE behavior will be specified.
      RAN1 chair will treat this together with dormancy discussion under MR-DC/CA WI
      RAN2 will wait for RAN1 conclusion. If it is agreed that additional behavior is needed for outside of active time, RAN2 chair will decide how to split the work between MC-DC/CA and Power Saving.
    MR-DC/CA and Power Saving WID will not be updated

## Slide 5: NR – Cont’d
Rel-16 MR-DC/CA in RP-192336, which added:
  Introduce support for aperiodic CSI-RS triggering with different numerology between CSI-RS and triggering PDCCH [RAN1]
  Introduce support for unaligned frame boundary with slot alignment and partial SFN alignment for R16 NR inter-band CA [RAN1, RAN2]
    Misalignment should be limited to ±76800Ts
    Signaling support for slot offset if necessary
  Note: Unaligned frame boundary is only allowed for certain band combination
  Note: Necessity of signaling support of slot offset should be discussed in RAN1
  Note: Blind detection of slot offset is not in scope
  Note: No optimization for MAC
  Note: Feature is optional and capability signaling is introduced by RAN2

## Slide 6: NR – Cont’d
Rel-16 Mobility WID in RP-192277, clarified that:
  To specify the following solutions agreed during the study phase. [RAN2/RAN1/RAN3/RAN4]:
    To reduce interruption time during HO:
      Dual active protocol stack based HO interruption time reduction solution;
    To improve HO/SCG change reliability and robustness:
      Conditional handover for NR PCell change;
      Conditional handover based NR PSCell addition/change for any architecture option with NR PSCell;
      T312 based fast failure recovery (similar to LTE)
Rel-16 2-step WID in RP-192330
  Specify contention-free 2-step RACH procedure (dedicated preamble and dedicated PUSCH) for handover (RAN2)
    RAN1 work addresses only CBRA (i.e. not considering CFRA)
    Note 3: The work on contention-free 2-step RACH procedure is of lower priority and should be pursued in RAN2 only if there is time.

## Slide 7: NR – Cont’d
Minor updates on some other existing Rel-16 WIs
  MIMO WID in RP-192271
    Addition of some details for RAN4 core requirements
    Removal “Specify UL transmit beam selection for multi-panel operation that facilitates panel-specific beam selection”
  CLI/RIM WID in RP-191997 (editorial-like updates)
  V2X WID in RP-191723 (editorial-like updates)
  IAB WID in RP-192188 (editorial-like updates)

## Slide 8: NR – Cont’d
RAN4-led WID on NR RF Requirement Enhancements for FR2 as approved in RP-192227 has RAN1 as secondary group
  RAN4 will provide further details on the RAN4 agreed solution(s) to RAN1/RAN2 before RAN1/RAN2 start their work if RAN1/RAN2 help is needed.
  This objective does not aim to propose the same alternatives which were not agreed (i.e. Alt1, Alt2 and Alt3 not agreed in RAN1#98 under Rel-16 NR eMIMO work item)
RAN4-led WID on RF requirements for NR frequency range 1 (FR1) as approved in RP-192282 now has RAN1 as secondary group
  RAN1 will further study by Dec 2019 if there are any RAN1 potential impacts based on RAN4 LS if any
    No new TDM pattern will be defined, i.e. scheduling-based switching is assumed.
    Finalization of RAN4 requirements and approval of RAN4 CRs shall be based on RAN1 LS
    Strive to minimize RAN1 impact.
    Strive to achieve no impact to RAN1 E-UTRAN spec
    Strive to avoid defining location of switching period impacting RAN1 spec

## Slide 9: NR – Cont’d
Sync NR-DC way forward was endorsed in RP-192345
  Introduce Rel-15 UE capability for SFN-sync
    To be implemented as a backward compatible CR based on the June specification version
      Omission of the bit means the UE is capable of slot aligned non-SFN-sync DC
      Inclusion of the bit means the UE is incapable of slot aligned non-SFN-sync DC
    Rel-16 UEs will not be allowed to use the bit defined in Rel-15
    RAN#87 (March/2020) to re-address the issue of mandating Release-15 UEs supporting NR-NR DC to support slot aligned non-SFN-sync DC
    There are no changes other than 38.306 and 38.331 for adding the UE capability
      Stage-2 description changes in 37.340 are not precluded
  The Rel-16 NR-NR DC scope is not changed

## Slide 10: Rel-17 Preparation
RAN#85 discussed email summaries of various topics, some intensively online & offline
The second phase of email discussion is to be carried out in the next quarter