## Slide 1: Comparison and WF on Spatial Consistency Methods
Huawei, HiSilicon
R1-161728
3GPP TSG RAN WG1 Ad Hoc meeting for Channel Model
Ljubljana, Slovenia, March 14-16, 2016
Agenda Item: 7

## Slide 2: Background
So far the contributions to AH channel modeling in Ljubljana, a total solution of spatial consistency is presented in the joint proposal R1-161622.
Three methods for the spatial consistency in R1-161622 are presented. All methods have supported simulations in separate proposals.
    Alternative 1: Method of using spatially consistent random variables (R1-161643)
    Alternative 2: Geometric stochastic approach (R1-161603)
    Alternative 3: Method using geometric locations of clusters (R1-161610)
Contribution of this proposal
    Summary of the three methods
    WF for spatial consistency
    Simulation of alternative 1 (see appendix)

## Slide 3: Summary of the three methods
 | Advantage | Disadvantage
Alternative 1 | Spatial consistent LSPs LOS/NLOS state Small changes to SCM Low complexity | Angles vary too fast for non-dominant clusters Cluster delays vary too fast No cluster birth and death No spherical wave support No mobility support Questionable beam tracking support
Alternative 2 | Correlated LSPs for close-by locations Reasonable time-variant angles Cluster birth/death Low complexity | Somehow discontinuity when moving from one grid square to another Hard LOS/NLOS transition
Alternative 3 | Highly realistic behavior for evolution of paths in delay/angle and for cluster birth/death | Challenging to devise methods that preserve channel statistics

## Slide 4: Proposals
Encourage members to resolve the problems of each method and provide solid simulations to verify the feasibility of the methods.
A harmonized model for spatial consistency is appreciated, or adopt one of the three alternatives for spatial consistency in future meetings.

## Slide 5
Appendix: Simulation results for Alternative 1

## Slide 6: Alternative 1 Results (1/5)
Method: Alternative 1 in R1-161622
  Complex normal distribution is used for the corner of one correlation grid
  Interpolation is used to generate the complex normal random variable
  Uniform distribution is generated from the phase of Y(x,y)
Simulation configuration: 3GPP SCM with fc=72GHz, 5 clusters in total, UE moves according to the trajectory with a certain interval.

## Slide 7: Alternative 1 Results (2/5)
Observations for LOS:
Angles gradually vary with positions, and the varying speed decreases as correlation distance increase
Angles (AoA, AoD) vary too fast for non-dominant clusters. The varying speed of AoA reaches 42.44 degree per meter in case of dcorr=50m, and 87.85 degree in case of dcorr=10m.

## Slide 8: Alternative 1 Results (3/5)
Observations for LOS:
Cluster delays gradually vary with position, and the varying speed decreases as correlation distance increase
Cluster delays vary too fast. The varying speed of delay reaches 80ns per meter in case of dcorr=50m, and 200 ns in case of dcorr=10m.

## Slide 9: Alternative 1 Results (4/5)
Observations for NLOS:
Angles gradually vary with position, and the varying speed increases as correlation distance increase
Angles (AoA, AoD) vary too fast in non-dominant clusters. The varying speed of AoA reaches 83.42 degree per meter in case of dcorr=50m, and 67. 5 degree per meter in case of dcorr=10m.

## Slide 10: Alternative 1 Results (5/5)
Observations for NLOS:
Cluster delay gradually vary with position, and the varying speed decreases as correlation distance increase
Cluster delays vary too fast. The varying speed of delay reaches 57.5ns per meter in case of dcorr=50m, and 225 ns per meter in case of dcorr=10m.