## Slide 1: WF on Time Evolution Modeling for >6GHz
Samsung, LGE, ETRI, Intel, Nokia, Ericsson, ALU, ASB
R1-161735
3GPP TSG RAN1 #AH Channel Model
Ljubljana, Slovenia, March 14 - 16, 2016
Agenda Item: 7

## Slide 2: Background – Channel generation equation
Channel coefficient generation for a given Tx, Rx and cluster is sum of responses of subpaths that can be decomposed into three parts:
    Field response: determined by multi-path component (MPCs) such as angles and powers as well as slant angle (polarization). Not dependent on antenna position!
    Array response: determined by antenna position and ray angles.
    Time evolution: Doppler for subpaths
In current channel model, the only thing changes across time is time evolution due to Doppler.
Note that a global coordinate system is assumed for the below equation.
Field response (dependent on polarization, multiple paths)
Array response (dependent on antenna position, element pattern)
Time evolution (dependent on Doppler)

## Slide 3: Background – Mobility Modeling in TR36.873
Assume movement of UE array is so small in the simulation duration and hence it does not change MPCs.
Then, current time evolution of Doppler already captures impact of position change:
  Denote , and the relative position of antenna as (corresponding to an absolute position and , respective). Also denote the unit directional vector of subpath as
  The change of array response for antenna is therefore:
  Note , the Doppler term in the channel coefficient equation, where is the speed projected onto the direction of .
y
x
z
Incident wave for a single subpath (far field)
Array moved from one position to another position.
d0=(x0,y0,z0)
d1=(x1,y1,z1)

## Slide 4: Proposal
The model should support drop-based evaluations irrespective of UE speeds.
The channel generation equation in 3GPP TR36.873 is reused for modeling time evolution of >6GHz channel modeling, at least those example cases below when drop-based evaluations are sufficient:
  Case 1: For low complexity evaluations
  Case 2: To compare with earlier simulation results,
  Case 3: When none of the additional modeling components are turned on.
  Case 4: When spatial consistency is modeled but UE’s position does not change in the simulations
  Other cases are not precluded

## Slide 5: Proposal
The model should support drop-based evaluations irrespective of UE speeds.
  Case 1: For low complexity evaluations
  Case 2: To compare with earlier simulation results,
  Case 3: When none of the additional modeling components are turned on.
  Case 4: When spatial consistency is modeled but UE’s position does not change in the simulations
  Other cases are not precluded
For drop-based simulations, the channel generation equation in 3GPP TR36.873 is reused